## Slide 1: In Lab Scenario 1 - Semester 1 2022 V1.1
Student ID: 103172423
Student Name: SM Ragib Rezwan
Session Time: (doing off time now for practise)
Tutor’s Name:

## Slide 2
Tandur
(Internal)
Router
R1
Tandur
Switch S3
3650
Corporate Network Address
158.VZ.0.0/16
In Lab Scenario 1 RIP Routing Protocol – V1.1
G0/0/1
S0/1/0
S0/1/0
RIPv2 Routing Protocol
Sedam
(Gateway)
Router
R2
G1/0/11
“The Internet”
Loopback 0
181.25.0.0/16
External Web Server 1
ISP
Router
R3
Trunk for Inter-VLAN
Routing
ISP Link
Network Address
201.24.4W.0/30
PC1
VLANXXX
PC2
VLANYYY
G1/0/13
Internal Serial
Loopback 0
Server LAN
Database Server
Network Topology
S0/1/1
S0/1/1
Loopback 3
211.31.8.0/24
External Web Server 4
All other web sites etc
A Network Configuration and Trouble Shooting Scenario
Internal
External
WRS1
Wireless
Router
G1/0/1
VLAN1
Internet Port
VLAN1
IP address
Mobile
Wireless
PC
Wireless
Connection
Loopback 1
22.0.0.0/8
External Web Server 2
Loopback 2
155.2.0.0/16
External Web Server 3
PC Ethernet VM
If in lab
PC VAN VM
If in lab

## Slide 3: The Scenario – An Analytical and Systematic Approach
The aim of this approach is to allow you to integrate the different topics (theory and practical) covered in the Unit, into the building of the network platform.
Each scenario requires you to build a working network, then add new network services and functionality to the network platform.
It is designed to be self re-enforcing, as what you have learnt in previous scenarios is required in future scenarios.
It emphasizes an Analytical and Systematic approach to building the network platform:
  Produce a Network Topology Diagram
  Prepare the VLSM Design
  Follow a step-by-step process to ensure that, configuration, testing, and troubleshooting is done in an order and sequence that will achieve a working network.
Doing the scenarios will prepare you for the Skills Tests
  Your tutor will provide advice and feedback only during your on campus Lab Session

## Slide 4
Scenario 1 Introduction
This scenario configuration details are provided on pages 13 to 23
Your tutor will give you an overview of the scenario
You can use Packet Tracer or book a Lab Kit
As a How to Configure Guide, it is recommended you obtain a copy of “CCNA Portable Commands Guide (CCNA Self-Study) 2/3/4/5 Ed”, Scott Empson, Cisco Press
What is new?
  Configuration of a dynamic routing protocol RIP (Routing Information Protocol) V2
  RIP V2 supports VLSM addressing
  Configuration of a static and a default route
  The integration of a Wireless network into the fixed infrastructure
Network Topology
  Internal, your internal network
  External, the link to the ISP and the Internet
  Use these Network addresses for Scenario 1, refer page 5 to determine V, Z and W
    Your Corporate Network Address is 158.VZ.0.0/16
    Your ISP Link Address is 201.24.4W.0/30

## Slide 5
How to determine your Network Addresses and VLAN Numbers
Rule Set A
Network Addresses – (Example Only, use your Student ID)
eg student Id
    Nine digit Id 123057210 (from Left to Right)
    If Seven digit Id 3057210 then 993057210 (from Left to Right)
  Rule 1: If the Corporate Network Address is 158.VZ.0.0/16 where V is seventh number and Z is last number in your student ID
    V=2 and Z=0, hence 158.20.0.0/16 is your Corporate Network Address
  Rule 2: If the ISP Link Address is 201.24.4W.0/30 where W is eighth number in your student ID
    W=1, hence 201.24.41.0 is your ISP Link Address
VLAN Numbers – (Example Only, use your Student ID)
  eg student Id
    Nine digit Id 123057210 (from Left to Right)
    If Seven digit Id 3057210 then 993057210 (from Left to Right)
  Rule 1: VLAN XXX where XXX are the last three numbers in you student ID
  Rule 2: VLAN YYY where YYY are the middle three numbers in you student ID
  Rule 3: IF XXX = YYY then XXX = XXX + 1
  Rule 4: VLAN 256 , IF XXX or YYY = 256 then 256 - 3 = 253
  Appling Rules
    Rule 1: VLAN XXX : XXX= 210 hence VLAN210
    Rule 2: VLAN YYY: YYY=057 hence VLAN57
    Rule 3: No need to apply
    Rule 4: No need to apply

## Slide 6
Scenario 1 Addresses and VLAN Numbers
Record your Network Addresses and VLAN Numbers
Refer Rule Set A
Your Student ID: 103172423
Your Corporate Network Address 158.VZ.0.0/16 V= 4 Z=3
Your ISP Link Address 201.24.4W.0/30 W= 2
Your VLAN Numbers
  XXX=423 YYY=172

## Slide 7: Task 2 VLSM Design – Use VLSM Calculator Paste Below
Order of hosts networks from max to min:
Network ……(……. hosts):
Now, test values to see how many bits we should keep for it: like 2,4,8,16,32,64,128,256,512,1024,2048, etc
(follow the list in subnet mask cheat sheet)
…..(value) <….(host given in question)
…..(value) >….(host given in question)
so we take ……. (the value just greater than no of hosts in question)
• How many usable IP addresses? ……. – 2 = ……..
How many host bit? …….= 2^…… So …….. host bits
How many network bits? 32- ……. = ….. bits
• Subnet mask in slash notation? /…..
• Network address =………./……
(………., so gap is ……. (256-…….=…..) in ….. octet. Se next subnet will be incremented by ……. in …..octet)
Network …… ( …… hosts): (repeat same with rest until end)

## Slide 8: Scenario 1 -Tasks
1. Do not configure enable passwords OR line console passwords on router and switches, unless specified by the task
2. Internal Network VLSM Design – Paste in page 7
a) IP VLSM Addressing Scheme and VLAN names and numbers:
  Refer rules page 6 to determine XXX and YYY
  VLAN XXX French 600 hosts
  VLAN YYY English 100 hosts
  VLAN 256 Hindi 50 hosts (256 may change, refer rules page 5)
  VLAN 1 18 hosts
  Internal Serial 2 hosts
  Sedam Database Server LAN loopback 0 40 hosts
b) Document assignment of ip addresses to router interfaces and PC Hosts
c) Use the VLSM calculator
3. Cable Connections – Refer Network Topology Diagram
a) Connect Tandur router interface G0/0/1 to Tandur switch port G1/0/11
b) Check routers are connected via serial links
c) Connect PC1 to G1/0/13 (In Lab use the patch panel), connect PC2 to G1/0/24 (In Lab use the VAN)
4. Helpful Configurations
a) Configure the line console on each router and switch, as shown below:
line console 0
logging synchronous (stops system messages overwriting your typing)
exec-timeout 0 0 (ensures you do not return to user executive mode)
b) Turn off DNS (Domain Name Service)
no ip domain-lookup (ensures if you miss-type a command, the router will not try to resolve the command as a URL web address)
5. Message of the Day (MOTD) Banner Configuration
Configure a MOTD Banner, recording your student id, family name and lab time, on all routers and switches, as shown below:
banner motd &
Welcome to Hostname
Your Student Id, Your Family Name, Your Session Time
&
6. Device Host Names
a) All devices must be configured with a host name eg TandurR1, TandurS1 etc

## Slide 9: Scenario 1 -Tasks
7. Switch Configuration S3 3650
a) Refer to pages 16 to 19 and to your journal and lab exercises from prior unit on Basic Switch and VLAN Configuration
b) Check the switch is clean, if NOT then:
i) Delete the vlan.dat file to remove old VLANs from the Switch, use - delete vlan.dat
ii) Use - erase startup-config then reload
c) Create VLAN XXX French, VLAN YYY English, VLAN 256 Hindi (256 may change, refer rules page 6)
d) Configure G1/0/11 as a trunk port
e) Configure as access ports, only VLAN XXX ports G1/0/13, G1/0/14 and VLAN YYY port G1/0/24
f) Switch Management – configure an ip address on interface VLAN1 and configure a default gateway IP address
g) Configure enable password cisco and Line vty with password cisco and login, so the switch can be accessed via Telnet
h) Configure Port Security only for VLAN XXX, mac address sticky on ports G1/0/13, G1/0/14 max 4, with violation protect
i) If In Lab Kit - Configure a static mac address on G1/0/24 use the MAC address of PC2
j) If Packet Tracer - configure Port Security, mac address sticky on G1/0/24 max 1, with violation shutdown
8. Trouble Shooting VLANs
a) To check VLANs created, use – show vlan brief
9. Trouble Shooting Port Security
a) To check port security is enabled, use - show port-security
b) A table will be displayed showing the security status of the switch ports
10. Network IP Address Configuration
a) Configure ALL router serial and loopback interfaces with ip addresses and descriptions
b) Tandur Router
i) Refer page 15 and to your journal and lab exercises from prior unit on Basic Inter-VLAN Routing
ii) Configure Inter-VLAN routing on G0/0/1
  Configure separate sub-interfaces for VLAN 1 (the management VLAN) and VLANs XXX and YYY
  Configure each sub-interface with an ip address and description
c) Configure PC1 and PC2 Hosts with specified VLAN
i) IP address and subnet mask.
ii) Default Gateway IP address.
d) Check default gateway configured on switch to Tandur router, use VLAN1 G0/0/1.1 sub-interface ip address
11. Trouble Shooting Trunking – between Switch and Router
a) To check Trunking is activated, on switch(es), use – show interface trunk
b) Check correct interface has been configured for trunking !

## Slide 10: Scenario 1 -Tasks
12. Trouble Shooting Point-to-Point Single Link Testing
a) This test is to check that each individual link in the network is working.
b) Ping (command) – ensure you can ping from one end of each link to the other:
  PC to Router in same subnet/VLAN/network.
  PC to PC in same subnet/VLAN/network.
  Router to each direct neighbour Router over a serial link.
c) Link NOT working ? - Common problems:
  Physical connection not made.
  The clock rate is not configured on DCE interface of a serial link.
  An incorrect IP address or subnet mask is configured on one interface of a link
  The interface is shutdown.
13. Trouble Shooting Inter-VLAN Routing Test
a) This test is to check Inter-VLAN routing is working
b) Ping PC1 – VLANXXX to PC2 – VLANYYY
c) Telnet PC1 to the switch S3
d) Check IP address/Mac address mapping on the router, show arp
14. Routing Protocol Configuration (refer pages 13,14)
a) Tandur
  RIP V2
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
b) Sedam
  RIP V2, do not advertise the external network address
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
  Configure default route to ISP Router
  Advertise default route to Tandur Router
c) ISP Router
  Do not configure RIP
  Only configure a static route (default class B mask) to your internal network
  Configure loopbacks to simulate ‘The Internet’

## Slide 11: Scenario 1 -Tasks
15. Trouble Shooting Routing - Presence of Subnets
a) Internal Routers
- Use show ip route to display the routing table on each router:
- Check all the subnets are present
- Check there is a default route
b) External Router
- Use show ip route to display the routing table:
- Check there is static route back to your internal network
c) Common problems:
  Routing protocol is not advertising a subnet
  An interface is down
  Static or Default route not configured
16. Trouble Shooting End-to-End Path Testing
a) This test is to check that the routing - static and dynamic, is working.
b) Ping from PC Hosts in VLAN XXX and VLAN YYY to External Web Servers - The Internet
c) Use traceroute to pin point problems.
d) Use debug ip icmp on ISP router to check ping request arrives
e) Check if a subnet is missing from a routing table, use - show ip route
f) End-to-End Path Test Failed ? - Common problems:
  Default gateway IP address not configured on a PC.
  PC connected to incorrect interface.
  Incorrect static route on ISP
  Subnet not advertised
  Default route not propagated/Gateway of last resort not set

## Slide 12: Scenario 1 -Tasks
17. Wireless Router Configuration
a) You will configure a Wireless Router and connect it to the fixed network infrastructure.
b) Refer to page 23 and Wireless Supporting Material
c) On WRS1 Wireless Router configure:
i) Internet Port with VLAN 1 IP address
ii) SSID as W<student id>
iii) DHCP to provide addresses for Wireless LAN PCs and your Mobile Phone
iv) allow inbound ping requests v) Do not configure wireless security
d) Connect a straight through UTP cable between Tandur Switch S3 G1/0/1 (port in VLAN1) and Internet Port (in VLAN1) on Wireless Router
e) VLAN 1 will carry wireless traffic
f) On ISP Router use – debug ip icmp
g) Configure a wireless end device to ping the Internet
h) From Wireless End Device, Ping the Internet

## Slide 13: Routing Configuration Rules
Each router should only advertise its internal directly connected networks
Routing updates must not be sent to LANs/VLANs
A default route to the Internet should only be configured on the gateway router
Only the gateway router must advertise the default route to the internal routers
The ISP router should have a static route pointing to the corporate’s Network Address with the relevant class A, B or C default mask
Do not configure the ISP router with a routing protocol

## Slide 14: RIP V2 Configuration
Configure on Tandur Router
router rip (The routing protocol))
version 2 (Version 2 supports VLSM)
network 158.VZ.0.0 (Advertise the internal network)
passive-interface G0/0/1.1 (Do not send routing updates to VLAN subnets)
passive-interface G0/0/1.XXX
passive-interface G0/0/1.YYY
Configure on Sedam Router (the gateway router)
ip route 0.0.0.0 0.0.0.0 S0/1/1 (Configure the default route to the Internet)
router rip
version 2
network 158.VZ.0.0
default-information originate (Advertise default route to other internal routers)
Configure on ISP Router (RIP is not configured on ISP)
ip route 158.VZ.0.0 255.255.0.0 S0/1/1 (ISP configure a static route to company’s network)

## Slide 15: Inter-VLAN Routing Configuration
Configure on the required Router
interface G0/0/1
description The Physical Interface
no shutdown
interface G0/0/1.1
description A logical Sub Interface
description VLAN 1 VLAN Management
encapsulation dot1q 1
ip address <dotted decimal> <subnet mask>
interface G0/0/1.<vlan id>
description A logical Sub Interface
description VLAN <vlan Id> <vlan name>
encapsulation dot1q <vlan id>
ip address <dotted decimal> <subnet mask>
etc ……

## Slide 16: Switch Configuration
Configure VLANs
vlan XXX
name French
vlan YYY
name English
vlan 256 (256 may change, refer rules page 7)
name Hindi
Configure IP address for management vlan 1
interface vlan 1
ip address <ip address> <mask> (This allows the switch to be configured remotely via Telnet)
Configure Default Gateway
ip default-gateway <ip address of router interface> (Use VLAN 1 subinterface IP address)

## Slide 17: 3650 Switch Configuration
Configure a switch ACCESS port (note you can specify a range of switch ports):
interface G1/0/13
switchport access vlan <number> (assigns port to a vlan)
switchport mode access (sets port to access, for PCs)
switchport port-security (enables port security, do not forget this command)
switchport port-security maximum 2 (maximum of 2 mac address(es) can stick)
switchport port-security mac-address sticky
switchport port-security violation shutdown (shuts down port, default when security turned on)
OR
switchport port-security violation protect (protects, but does not shut down the port)
Configure a static MAC address entry in Mac Address Table
mac address-table static AAAA.BBBB.CCC vlan YYY interface G1/0/24
(replace AAAA.BBBB.CCCC with the mac address of the PC)

## Slide 18: Switch Configuration
Configure a switch TRUNK port on a Switch
2960 Series Switch
interface G0/1
switchport mode trunk (sets port to trunk)
3650 Series Switch
interface G1/0/11
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation)
switchport mode trunk (sets port to trunk)
3560 Series Switch
interface Fa0/1
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation)
switchport mode trunk (sets port to trunk)

## Slide 19: Switch Commands
Managing the MAC Address Table
show mac address-table (displays entries in table)
show mac address-table dynamic (displays only dynamic entries in table)
clear mac address-table (deletes all entries from table)
clear mac address-table dynamic (deletes only dynamic entries from table)
Re-activating a switch port that has been violated
When a violation causes a switch port to block traffic, it must be re-activated
This is achieved by doing a shutdown then a no shutdown on the switch port, refer example below:
interface G1/0/13
shutdown
(wait until shutdown confirmed)
no shutdown

## Slide 20: How to configure SSH – Secure Shell
1. Configure switch or router with a hostname:
hostname S1
2. Configure a local user account:
username labuser privilege 15 secret cisco
3. Configure domain name:
ip domain-name scenario.lab
4. Configure SSH Certificate:
crypto key generate rsa general-keys modulus 1024
5. Configure Line vty
line vty 0 15 (4 for a router)
transport input SSH
login local
end

## Slide 21: PC Command Window Useful Trouble Shooting Commands
ipconfig
  Allows you check your PC’s addresses
  ipconfig /all
  ipconfig /? for help
netstat
  Displays the TCP/IP network protocol statistics and information
  netstat –a
  netstat –e
  netstat –s
  netstat /? for help
nbtstat
  Displays protocol statistics and current TCP/IP connections
  nbtstat –n
  nbtstat /? for help

## Slide 22: PC Command Window Useful Trouble Shooting Commands
arp
  Displays the Address Resolution table
  arp -a
  arp /? for help
route print
  Displays the routing table of your PC
  route /? for help
ping
  ping 127.0.0.1 - Checks your PC’s IPv4 Protocol stack
  ping 192.168.1.10 - ping a destination
  ping /? for help
tracert
  Traces individual hops to the destination
  tracert 192.168.1.10
  tracert /? for help

## Slide 23: In Lab - Configuring the Wireless Router – Linksys WRT300N Also refer Wireless Supporting Material A and B
Power UP wireless router (get a wireless router from your tutor)
Reset it to factory default – push reset button and hold until blue symbols flash
Start up PC Ethernet VM, configure to obtain ip address automatically
Ethernet Connection – plug blue UTP cable from your PC into any Ethernet port (1 to 4) on the wireless router
Open DOS Command Window – type ipconfig /all to confirm PC Ethernet has been obtained an ip address from wireless router
Use a Browser to connect to factory default ip address 192.168.1.1 on the wireless router
Authentication – username: admin, password: admin
Wireless Router Setup
  Ensure you always click save at the bottom of each screen
  Internet Setup
    Internet Connection type: static IP
    Assign an ip address from VLAN 1 address range
  Network Setup - DHCP
    For Wireless PCs
    Use address space for wireless LAN
  Disable/Enable PC Ethernet LAN connection to pick up a new ip address from Wireless LAN address space
  Use a Browser to re-connect to new (default gateway) ip address on the wireless router
  Security
    Disable Firewall
  Wireless Wi-Fi Protected Setup
    Wireless Configuration: manual
    SSID: student Id
Use a Wireless End Device to connect to the Wireless Router refer below:
  Look for the wireless tray icon – bottom right, click
  Associate with the wireless LAN broadcasting your student ID as its SSID
  Open DOS Command Window – type ipconfig /all to confirm an ip address has been obtained from wireless router
  From your Laptop PC Ping default gateway on the wireless router to confirm connection is working
  Wireless Router - Remove blue UTP cable from your PC, get a new blue UTP cable, plug into Internet Port
  Connect new blue UTP cable to Desk Top coloured enclosure port, then patch from patch panel to Tandur switch port G1/0/1
  From your Laptop PC Ping to default gateway for VLAN 1 to confirm the connection is working