## Slide 1: TNE20002/TNE70003
Topic 1: Routing

## Slide 2: The Router
Routers
are the
core
of
The Internet

## Slide 3: Routing
The Internet is too large to have all hosts together as one network, it is subdivided
Internet

## Slide 4: Routers connect Networks
The Internet is subdivided into many separate networks.
Each router interface Fa0/0, S0/0/0, etc is a Gateway to another a network
Network 1
IPv4 Class A 18.0.0.0/8
Network 2
IPv4 Class B 140.16.0.0/16
Network 3
IPv4 Class C 192.10.30.0/24
Fa0/0
S0/0/0
Internet
Switch
Switch
S0/0/1
Fa0/1

## Slide 5: The Router
The router, routes IP packets to the intended destination
The router, drops IP packets to reduce congestion
  Setting Time to Live (TTL) to 10 hops, means if the packet cannot reach its destination within 10 hops, it will be dropped
  When a packet enters a router, deduct 1 from TTL
  IF TTL = 0 the packet will be dropped

## Slide 6
Nova
Router
R1
Nova
Switch S1
3650
Address Space
IPv4 Class B 172.16.0.0/16
G0/1
S0/1/1
S0/1/0
Magda
Router
R3
G1/0/11
Sydney
Router
R4
Inter-VLAN
Routing
PC1
VLAN77
PC2
VLAN55
G1/0/13
Fa 0/24
Network Topology
S0/2/0
S0/1/0
Jatai
Router
R2
Jatai
Switch S2
2960
Inter-VLAN
Routing
G0/0/1
G0/0/1
S0/1/1
S0/1/1
S0/1/0
S0/1/0
<- Hop 
Routing Protocol
RIPv2
<- Hop 
<- Hop 
<- Hop 
182.16.77.0/24
182.16.55.0/24
Inter-VLAN
Routing
Sydney
Switch S4
2960
G0/0/1
G0/1
PC3
VLAN66
182.16.66.0/24
Fa 0/24

## Slide 7: IP Header TTL
TTL

## Slide 8: Routing Decisions
Based on the Information in the Routing Table, the Router
Makes a Best Match Decision
  It determines the Best Match, between the destination network address in the incoming packet and a network address entry in the routing table
Makes a Forwarding Decision
  It determines the correct exit interface then forwards the packet to that exit interface (R1 S0/1/1 pg 6), towards the destination network.

## Slide 9: The Router - Best Match Decision
The Best Match is the one that has the most number of bits (left to right) matching between the destination IP network address and a routing entry in the Routing Table.
Best
Best
26 bits Match
26 bits
18 bits
12 bits
26 bits

## Slide 10: Routing Decisions – Flow Chart
Search for
Best Match
Destination Unknown
Default Route
Local Subnet
Forwarding
Correct
EXIT Interface
Notes: 1.2.2.1 Routing Decisions

## Slide 11
Router ARP Table – Local Subnets
Forwarding a packet through FastEthernet Interfaces
Display ARP Table on Router - show arp (Mapping IP to Mac)
Two Local Subnets
100.25.34.0/24
100.25.44.0/24
44.10
34.25

## Slide 12
PC ARP Table
Display ARP Table on PC in Command Window - arp -a

## Slide 13: The Router
The
Routing
Protocol

## Slide 14: Path Determination - Least Cost Path
The Least Cost Path to a given network is determined by a routing protocol calculating the cost.
The cost calculation can involve a number of metrics.
The Least Cost Path to a network is the path with the lowest cost.
Notes: 1.2.2.2 Best Path

## Slide 15: Metrics
Hop Count: counts the number of routers a (IP) packet must traverse
Bandwidth: Influences path selection by preferring the path with the highest bandwidth
Load: Considers the traffic utilization of a link
Signal Delay: Considers the time a packet takes to traverse a path
Reliability: Assesses the probability of a link failure

## Slide 16: Cost
The
COST
is
calculated
based on the
metrics
used by the
Routing
protocol

## Slide 17: Dynamic Routing Protocols
Routing Information Protocol
RIP
cost
based on metric
Hop count
Notes: 1.2.2.2 Best Path

## Slide 18: Dynamic Routing Protocols
Open Shortest Path First
OSPF
cost
based on metric
bandwidth
from source to destination
Notes: 1.2.2.2 Best Path

## Slide 19: Dynamic Routing Protocols
Enhanced Interior Gateway Routing Protocol
EIGRP
cost
based on metrics
Bandwidth, delay, load, reliability
Notes: 1.2.2.2 Best Path

## Slide 20: Routing Table - Least Cost Paths
Only the
Least Cost paths
to given destination networks,
as determined by a routing protocol,
are placed in
the routing table
Notes: 1.2.2.2 Best Path

## Slide 21: The Router
The
Routing
Table

## Slide 22: The Routing Table – R1
A routing table for R1 is a file stored in RAM that contains information about:
  Directly connected routes
  Remote routes (learnt via routing protocol)
  Next hop associations
Notes: 1.3.1.1 The Routing Table

## Slide 23: Routing Table Entries – show ip route
Link local route interfaces - Added to the routing table when an interface is configured. Shows IP address of the Interface.
Connected interfaces - Added to the routing table when an interface is configured and active.
Static routes - Added when a route is manually configured and the exit interface is active.
Dynamic routes - Added when RIP, EIGRP or OSPF are implemented and networks are identified.
Notes: 1.3.1.2 Routing Table Sources

## Slide 24: Directly Connected Routes – R1
An active, configured, directly connected interface creates two routing table entries:
Link Local (L) and Connected (C)
Notes: 1.3.2.2 Directly Connected Interfaces

## Slide 25: Routing Table Entries – R1: Remote Network
Remote Network
Notes: 1.3.1.2 Routing Table Sources

## Slide 26: Routing Table Entries – R1: Remote Network
Interpreting the entries in the routing table.
D - EIGRP
Remote Network
Notes: 1.3.1.3 Remote Network Routing Entries

## Slide 27
THE END