## Slide 1: Topic 10 Multi-Area OSPF V1.0
TNE20002/TNE70003
Notes: 8.1 Multiarea OSPF Operation

## Slide 2: Why Multi-Area OSPF?
Single-area OSPF is useful in smaller networks.
If an area becomes too large (Cisco state an area should have no more than 50 routers), the following issues must be addressed:
  Large routing table
  Large link-state database (LSDB)
  Frequent SPF algorithm calculations
Notes: 8.1.1.1 Single-Area OSPF

## Slide 3: Why Multi-Area OSPF?
Single Area 0

## Slide 4: Multi-Area OSPF
Regular
Backbone
Regular
Notes: 8.1.1.2 Multiarea OSPF

## Slide 5: OSPF Two-Layer Area Hierarchy
Multiarea OSPF is implemented in a two-layer area hierarchy:
  Backbone (transit) area
    Area whose primary function is the fast and efficient movement of IP packets.
    Called OSPF area 0, to which all other areas directly connect.
  Regular (non backbone) area
    Connects users and resources.
    A regular area does not allow traffic from another area to use its links to reach other areas.
Notes: 8.1.1.3 OSPF Two-Layer Area Hierarchy

## Slide 6: Multi-Area OSPF
Regular
Backbone
Regular
Notes: 8.1.1.2 Multiarea OSPF

## Slide 7: Types of OSPF Routers
Internal Router
Backbone Router
Area Border Router (ABR)
Autonomous System Boundary Router (ASBR)
A router can have multiple roles

## Slide 8: Types of OSPF Routers - Internal
All interfaces in the same area
All routers within the same area have identical LSDBs
External Autonomous System
Notes: 8.1.1.4 Types of OSPF Routers

## Slide 9: Types of OSPF Routers - Backbone
Routers that sit within the perimeter of backbone area 0 and
have at least one interface connected to area 0
External Autonomous System
Notes: 8.1.1.4 Types of OSPF Routers

## Slide 10: Types of OSPF Routers – Area Border
Routers that have interfaces attached to multiple areas
Maintain separate LSDBs for each area, and route traffic between areas
R1iR1
R1ttt
External Autonomous System
Notes: 8.1.1.4 Types of OSPF Routers

## Slide 11: Types of OSPF Routers – Area Border
  ABRs connect area 0 to a non backbone area
  Are exit points for an area
  Routing information destined for another area can get there only via the ABR of the local area
  ABRs distribute routing information into backbone
  Backbone routers forward routing information to other ABRs
  ABRs are the only point where address summarization can be configured, to summarize the routing information from the LSDBs of their attached areas
Notes: 8.1.1.3 OSPF Two-Layer Area Hierarchy

## Slide 12: Types of OSPF Routers – Autonomous System Boundary
Routers that have at least one interface attached
to a different routing domain eg EIGRP
EIGRP
External Autonomous System
Notes: 8.1.1.4 Types of OSPF Routers

## Slide 13: Types of OSPF Routers – Autonomous System Boundary
  Different Routing Domains
    A domain using EIGRP
  ASBRs can redistribute external EIGRP routes into the OSPF domain
Notes: 8.1.1.3 OSPF Two-Layer Area Hierarchy

## Slide 14: Types of OSPF Routers
Internal Router
  All interfaces in the same area
Backbone Router
  Routers that sit within the perimeter of backbone area 0 and have at least one interface connected to area 0
Area Border Router (ABR)
  Routers that have interfaces attached to multiple areas
Autonomous System Boundary Router (ASBR)
  Routers that have at least one interface attached to a different routing domain eg EIGRP

## Slide 15: OSPF LSA (Link State Advertisement) Types
The building blocks of OSPF, Only 1 to 5,
will be covered
Notes: 8.1.2.1 OSPF LSA Types

## Slide 16: Type 1 - Router LSA
Every router generates Type 1 LSAs for each area to which it belongs
Describes the states of the router’s links to the other routers in the area and are flooded only within a particular area
Notes: Chapter 8 Summary

## Slide 17: Type 1 - Router LSA

## Slide 18: Type 1 - Router LSA
EIGRP External Autonomous System
Notes: 8.1.2.2 OSPF LSA Type 1

## Slide 19: OSPF – Router ID
To use OSPF a Router must have a Router ID to identify the router within the OSPF network; it uses an IP address as its ID
Routers have multiple IP addresses, which one should be used?
Router ID is derived based on 3 criteria in order of precedence:
  Configured using OSPF router-id command
  If router-id command not used, router chooses highest IP address of any loopback interfaces.
  If no loopback interfaces are configured, the highest IP address on any active interface is used

## Slide 20: Type 2 - Network LSA – Multi Access Networks
DRs (Designated routers) generate Type 2 network LSAs for multi-access networks
Describe the set of routers attached to a particular multi-access network
Are not forwarded outside of an area
Notes: Chapter 8 Summary

## Slide 21: Type 2 - Network LSA – Multi Access Networks
Designated router (DR) and
Backup designated router (BDR)
Sending and Receiving LSAs
Router R1 sends Type 1 LSAs via multicast 224.0.0.6 to DR & BDR
DR sends Type 2 LSA via multicast address 224.0.0.5 to DRothers (all other routers)
Type 1 From R1
DRothers
Type 2 From DR

## Slide 22: Operation OSPF LSA Type 2
Multi-access links
Serial links
Network
External Autonomous System
Notes: 8.1.2.3 OSPF LSA Type 2

## Slide 23: How do we Learn about networks in other Areas?
Type 3 Summary LSA
Type 4 Summary LSA
ABRs are the only point where address summarization can be configured, to summarize the routing information from the LSDBs of there attached areas
Do not cause a router to run SPF algorithm

## Slide 24: Type 3 - Summary LSA
Describe interarea routes
Describe routes to an area’s networks, may include summary routes, are created and generated by ABR.
Notes: Chapter 8 Summary

## Slide 25: OSPF LSA Type 3
Multi-access links
Serial links
Summary
EIGRP External Autonomous System
Type 1
Notes: 8.1.2.4 OSPF LSA Type 3

## Slide 26: Type 3 - Summary LSA
An Area Border Router (ABR) takes information it has learned on one of its attached areas and summarizes it before sending it out to other areas it is connected to
This summarization provides scalability by removing detailed topology information for other areas, because their routing information is summarized into just an network address, prefix and cost.

## Slide 27: Type 4 – ASBR Summary LSA
Is generated by an ABR only when an Autonomous System Boundary Router exists within an area.
Provides the route to the ASBR (Router), to routers in other areas
.
Notes: Chapter 8 Summary

## Slide 28: Multiarea OSPF LSA Operation OSPF LSA Type 4
Multi-access links
Serial links
Summary
EIGRP External Autonomous System
Learned from Type 1
Notes: 8.1.2.5 OSPF LSA Type 4

## Slide 29: Type 5 - Autonomous System External LSA
Describe routes to networks outside the OSPF autonomous system.
Generated by the ASBR and are flooded to the entire autonomous system.
Notes: Chapter 8 Summary

## Slide 30: OSPF LSA Type 5
Multi-access links
Serial links
External
EIGRP External Autonomous System
Notes: 8.1.2.6 OSPF LSA Type 5

## Slide 31: OSPF – Steps to Convergence
Calculate Intra Area OSPF Routes
All routers via LSAs type 1 and 2,
calculate via SPF algorithm
the least cost paths to destinations
within their area (intra-area)
and add these entries to the routing table.
Designator O in routing table
Notes: 8.1.3.2 OSPF Route Calculation

## Slide 32: OSPF – Steps to Convergence
Inter Area OSPF Routes
All routers via LSAs type 3 and 4
receive the least cost paths to the
networks in other areas
within the internetwork (inter-area) .
Designator O IA in routing table
Notes: 8.1.3.2 OSPF Route Calculation

## Slide 33: OSPF – Steps to Convergence
OSPF Routes to External Non OSPF Networks
All routers via LSA type 5,
receive the least paths to the external
autonomous system destinations.
Designator O E2 in routing table
Notes: 8.1.3.2 OSPF Route Calculation

## Slide 34: OSPF – 3 Steps to Convergence – Routing Table
1
2
3
Calculate via SPF least cost paths to intra-area routes
Insert least cost paths to inter-area networks
Insert least cost paths to external non-OSPF networks
Notes: 8.1.3.2 OSPF Route Calculation

## Slide 35: OSPF Routing Table Entries
  O – Router describe the details within an area (the route is intra-area).
  O IA – Summary inter-area routes
  O E2 – External routes
Notes: E1 or External Type Routes – The cost of E1 routes is the cost of the external metric with the additional of the internal cost within OSPF to reach that network. ... Basically difference between E1 and E2 is: E1 includes – internal cost to ASBR added to external cost, E2 does not include – internal cost

## Slide 36
The END
OSPF Multi Area Explained - YouTube