## Slide 1: TNE20002/TNE70003
Topic 2: RIP Routing Protocol
V1.0

## Slide 2: Routing Protocols
Routing Protocols
facilitate
the exchange of
routing information
between routers
Notes: 3.1.1.2 Purpose of Dynamic Routing Protocols

## Slide 3: Routing Protocols
Discover remote networks
Determine least cost paths to destination networks
Maintain up-to-date routing information in tables
Find a new least cost path if the current path is no longer
available
Notes: 3.1.1.2 Purpose of Dynamic Routing Protocols

## Slide 4: Routing Protocols
Main components include:
Data structures – A Routing Protocol uses tables for its operations. These tables are stored in RAM.
Routing protocol messages
  To discover neighboring routers,
  To exchange routing information,
  To learn and maintain accurate information about the
  network.
Algorithm - for least cost path determination.
Notes: 3.1.1.2 Purpose of Dynamic Routing Protocols (cont.)

## Slide 5: Routing Protocols
The routing table
contains
only
the least cost paths
to destination networks
Notes: 3.1.1.2 Purpose of Dynamic Routing Protocols

## Slide 6: Routing Protocols: Network Convergence
The network has converged when all routers have complete and accurate information (in their tables) about the network topology.
Not Instantaneous
It takes time for routers to
  share information (collaborate with other routers),
  determine least cost paths (independent of other routers),
  update their tables

## Slide 7
From
COLD Start
To
Network Convergence
Routing Protocols – RIP
Notes: 3.1.3.5 Achieving Convergence

## Slide 8: Operation - Cold Start
Routers running RIPv2
Directly Connected Networks Detected and Added to Routing Table
R1
R2
R3
Hop
Notes: 3.1.3.2 Cold Start

## Slide 9: Operation - Cold Start
R1 adds the 10.1.0.0 network available through Fa0/0 and 10.2.0.0 is available through S0/0/0.
R2 adds the 10.2.0.0 network available through S0/0/0 and 10.3.0.0 is available through S0/0/1.
R3 adds the 10.3.0.0 network available through S0/0/1 and 10.4.0.0 is available through Fa0/0.
Directly Connected Networks Detected and Added to Routing Table
Notes: 3.1.3.2 Cold Start

## Slide 10: Operation – Exchanging Information
R1:
Sends an update about network 10.1.0.0 out S0/0/0
Sends an update about network 10.2.0.0 out Fa0/0
Receives update from R2 about network 10.3.0.0 with a cost of 1 hop
Stores network 10.3.0.0 in the routing table with a cost of 1 hop
Routers running RIPv2
Notes: 3.1.3.3 Network Discovery

## Slide 11: Operation - Exchanging Information
R2:
Sends an update about network 10.3.0.0 out S0/0/0
Sends an update about network 10.2.0.0 out S0/0/1
Receives an update from R1 about network 10.1.0.0 with a cost of 1
Stores network 10.1.0.0 in the routing table with a cost of 1
Receives an update from R3 about network 10.4.0.0 with a cost of 1
Stores network 10.4.0.0 in the routing table with a cost of 1
Routers running RIPv2
Notes: 3.1.3.3 Network Discovery (cont.)

## Slide 12: Operation - Exchanging Information
R3:
Sends an update about network 10.4.0.0 out S0/0/1
Sends an update about network 10.3.0.0 out Fa0/0
Receives an update from R2 about network 10.2.0.0 with a cost of 1
Stores network 10.2.0.0 in the routing table with a cost of 1
Routers running RIPv2
Notes: 3.1.3.3 Network Discovery (cont.)

## Slide 13: Operation – Exchanging Information
R1:
Sends an update about network 10.1.0.0 out the S0/0/0
Sends an update about networks 10.2.0.0 and 10.3.0.0 out the Fa0/0
Receives an update from R2 about network 10.4.0.0 with a cost of 2
Stores network 10.4.0.0 in the routing table with a cost of 2
Routers running RIPv2
Notes: 3.1.3.4 Exchanging the Routing Information

## Slide 14: Operation - Exchanging Information
R2:
Sends an update about networks 10.3.0.0 and 10.4.0.0 out S0/0/0
Sends an update about networks 10.1.0.0 and 10.2.0.0 out S0/0/1
Receives an update from R1 about network 10.1.0.0. There is no change, therefore, the routing information remains the same.
Receives an update from R3 about network 10.4.0.0. There is no change, therefore, the routing information remains the same.
Routers running RIPv2
Notes: 3.1.3.4 Exchanging the Routing Information (cont.)

## Slide 15: !! Convergence Achieved !!
R3:
Sends an update about network 10.4.0.0 out S0/0/1
Sends an update about networks 10.2 0.0 and 10.3.0.0 out Fa0/0
Receives an update from R2 about network 10.1.0.0 with a cost of 2
Stores network 10.1.0.0 in the routing table with a cost of 2
Receives an update from R2 about network 10.2.0.0 with a cost of 1. There is no change; therefore, the routing information remains the same.
Routers running RIPv2
Notes: 3.1.3.4 Exchanging the Routing Information (cont.)

## Slide 16: RIPv2

## Slide 17: RIPv2
RFC 1723 – 1994, RFC 2453 - 1998
Uses well known port 520
Administrative distance 120
Metric Hop Count
Maximum Hop Limit 15
Supports VLSM, includes subnet mask in RIP update
Next hop address is included in update
Periodic updates every 30 secs
Triggered updates on link failure
Routing updates are multicast, 224.0.0.9
Use debug ip rip to view multicasting of updates
The use of authentication is an option

## Slide 18: Comparing RIPv2 & RIPv1 Message Formats
RIPv2 Message format has extensions:
  A subnet mask field
  The addition of next hop address

## Slide 19: RIPv2 – Updates include (VLSM) Subnet Masks
Use the debug ip rip

## Slide 20: Enabling RIPv2
Notes: 3.3.1.4 Enabling RIPv2

## Slide 21: RIPv2 – Advertising Directly Connected Networks
R1(config)# router rip
R1(config-router) version 2
R1(config-router) network 192.168.1.0
R1(config-router) network 192.168.2.0
R2(config)# router rip
R2(config-router) version 2
R2(config-router) network 192.168.2.0
R2(config-router) network 192.168.3.0
R2(config-router) network 192.168.4.0
R3(config)# router rip
R3(config-router) version 2
R3(config-router) network 192.168.4.0
R3(config-router) network 192.168.5.0
The network Command:
Specifies network to be advertised
Enables RIP on all interfaces that belong to the networks
You advertise, only the directly connected networks, on any given router

## Slide 22: Configuring Passive Interfaces R1
Sending out unneeded updates to LANs impacts the network:
Wasted Bandwidth on Link
Wasted CPU Resources on PCs
Security Risk, routing tables reveal network topology
PC1
PC2
PC3
Notes: 3.3.1.6 Configuring Passive Interfaces

## Slide 23: R1 Gateway Propagating a Default Route to R2,R3
Notes: 3.3.1.7 Propagating a Default Route

## Slide 24
Tandur
(Internal)
Router
R1
Tandur
Switch S3
3650
Corporate Network Address
158.VZ.0.0/16
In Lab Scenario 1 RIP Routing Protocol – V1.0
G0/0/1
S0/1/0
S0/1/0
RIPv2 Routing Protocol
Sedam
(Gateway)
Router
R2
G1/0/11
“The Internet”
Loopback 0
181.25.0.0/16
External Web Server 1
InLabScenario1_RIP_S2_2021_V1.0.pptx
ISP
Router
R3
Trunk for Inter-VLAN
Routing
ISP Link
Network Address
201.24.4W.0/30
PC1
VLANXXX
PC2
VLANYYY
G1/0/13
Internal Serial
Loopback 0
Server LAN
Database Server
Network Topology
S0/1/1
S0/1/1
Loopback 3
211.31.8.0/24
External Web Server 4
All other web sites etc
A Network Configuration and Trouble Shooting Scenario
Internal
External
WRS1
Wireless
Router
G1/0/1
VLAN1
Internet Port
VLAN1
IP address
Mobile
Wireless
PC
Wireless
Connection
Loopback 1
22.0.0.0/8
External Web Server 2
Loopback 2
155.2.0.0/16
External Web Server 3
PC Ethernet VM
If in lab
PC VAN VM
If in lab

## Slide 25: END