## Slide 1: Topic 3 ACLs V1.1
S1 2022

## Slide 2: Addressing
Network 145.60.0.0/16
VLAN10 Marketing 80
VLAN20 Sales 50 hosts
Server Farm 20 hosts
VLAN99 TechSupport 10 hosts
Internal Serial Link 2 hosts
Link to ISP 200.10.10.0/30
R3 Loopback0 170.20.0.0/16 external site
External Server Site 150.20.0.0/16

## Slide 3
Subnet Name | Needed Size | Allocated Size | Address | Mask | Dec Mask | Assignable Range | Broadcast
VLAN10 | 80 | 126 | 145.60.0.0 | /25 | 255.255.255.128 | 145.60.0.1 - 145.60.0.126 | 145.60.0.127
VLAN20 | 50 | 62 | 145.60.0.128 | /26 | 255.255.255.192 | 145.60.0.129 - 145.60.0.190 | 145.60.0.191
Server Farm | 20 | 30 | 145.60.0.192 | /27 | 255.255.255.224 | 145.60.0.193 - 145.60.0.222 | 145.60.0.223
VLAN99 | 10 | 14 | 145.60.0.224 | /28 | 255.255.255.240 | 145.60.0.225 - 145.60.0.238 | 145.60.0.239
Internal Serial | 2 | 2 | 145.60.0.240 | /30 | 255.255.255.252 | 145.60.0.241 - 145.60.0.242 | 145.60.0.243
Subnetting Successful
Major Network: 145.60.0.0/16 Available IP addresses in major network: 65534 Number of IP addresses needed: 162 Available IP addresses in allocated subnets: 234 About 0% of available major network address space is used About 69% of subnetted network address space is used
VLSM

## Slide 4: Extended Named ACL For VLAN 10 on R1
1) Addresses
ISP Packet Tracer Server0 150.20.0.2
VLAN 10 145.60.0.0 /25 Mask 255.255.255.128 Wildcard (inverse of mask) 0.0.0.127
2) Rules for VLAN 10
Rule 1 - Deny ONLY HTTP access to ISP Packet Tracer Server0
Rule 2 - Permit ALL other access to ISP Packet Tracer Server0
3) ACL for VLAN 10
ip access-list extended ACLVLAN10
deny tcp 145.60.0.0 0.0.0.127 host 150.20.0.2 eq 80
permit ip any any
4) ACL Placement for VLAN 10
interface G0/0/1.10
ip access-group ACLVLAN10 in

## Slide 5: Extended Named ACL For VLAN 20 on R1
1) Addresses
ISP Packet Tracer Server0 150.20.0.2
VLAN 20 145.60.0.128/26 Mask 255.255.255.192 Wildcard (inverse of mask) 0.0.0.63
2) Rules for VLAN 20
Rule 1 - Permit ONLY HTTP access to ISP Packet Tracer Server0
Rule 2 - Deny ALL other access to ISP Packet Tracer Server0
Rule 3 - Permit ALL other access
3) ACL for VLAN 20
ip access-list extended ACLVLAN20
permit tcp 145.60.0.128 0.0.0.63 host 150.20.0.2 eq 80
deny ip 145.60.0.128 0.0.0.63 host 150.20.0.2
Permit ip any any
4) ACL Placement for VLAN 20
interface G0/0/1.20
ip access-group ACLVLAN20 in

## Slide 6: Extended Named ACL Structure
deny|permit protocol source ip source wildcard [operator operand] destination ip destination wildcard [operator operand]
  protocol
    ip – Matches all protocols (includes IP,TCP, UDP, ICMP etc.)
    icmp – Matches ICMP protocol
    tcp – Matches TCP protocol
    udp – Matches UDP protocol
  Source ip source wildcard
    Matches packet source IP Address
  Destination ip destination wildcard
    Matches packet destination IP Address
Notes: 6

## Slide 7: Extended Named ACL Structure
operator
eq, neq – Port number equal or not equal to specified operand
lt, gt – Port number less or greater than specified operand
and
operand
Integer port number eg 80, 20, 23
Text representation of service name eg. http, ftp, telnet
Notes: 7

## Slide 8: Extended Named ACL
Create the ACL in Notepad, then paste into router config mode
no ip access-list extended ACLVLANXXX (Delete previous version of the ACL for VLAN XXX )
Ip access-list extended ACLVLANXXX (Self-documenting, the ACL for VLAN XXX, ! means comment)
ACL Case Sensitivity
ACL names are case sensitive eg aclvlan70 and AclVlan70 are different ACLs
Should decide to use either all uppercase - ACLVLAN70 or all lowercase – aclvlan70 names to reduce errors
ACL Rule Order
ACL rules in the access list should be in order of most specific to least specific
The last rule should be permit All other access
ACL Placement Rule
Extended ACL – place as close as possible to source network or device, to block traffic early to reduce network congestion

## Slide 9: Extended Named ACL Trouble Shooting
It is important to verify that the ACL rules actually work as intended, refer to the steps below:
  1. Use show access-lists
    If all rules tested go to 5
    Else Identify which rule you want to test
  2. Use clear access-list counters
    Clear any counts against the rules
  3. Go to PC in VLAN<Id> perform test eg Ping, Telnet, Browser etc to trigger a match with the identified rule
  4. Use show access-lists
  Was the identified rule matched ?
    Yes – rule action correct, Repeat process, go to 1
    No – Debug
      Was another rule matched ?
      Where no rules matched ?
      Check syntax and order of rules – make changes – Repeat process go to 1
5. Trouble Shooting completed

## Slide 10: Standard Named ACL – Telnet Remote Access to R2
1) Addresses
VLAN 10 145.60.0.0 /25 Mask 255.255.255.128 Wildcard (inverse of mask) 0.0.0.127
VLAN 20 145.60.0.128/26 Mask 255.255.255.192 Wildcard (inverse of mask) 0.0.0.63
R2 S0/1/0 IP Address 145 .60.0.242
2) Rules for VLAN 10
Rule 1 - Deny Telnet Access to R2
3) Rules for VLAN 20
Rule 1 – Permit Telnet Access to R2
4) Configuration on R2
ip access-list standard ACLTELNETACCESS
! VLAN 10
deny 145.60.0.0 0.0.0.127
! VLAN 20
permit 145.60.0.128 0.0.0.63
5) ACL Placement on R2
line vty 0 4
password cisco
login
access – class ACLTELNETACCESS in
i

## Slide 11: Standard Named ACL
Create the ACL in Notepad, then paste into router config mode
no ip access-list standard ACLTELNETACCESS
! (Delete previous version of the ACL )
Ip access-list standard ACLTELNETACCESS
! (Self-documenting, the ACL for Telnet Access , ! means comment)
ACL Case Sensitivity
ACL names are case sensitive
Should decide to use either all uppercase or all lowercase names to reduce errors
ACL Rule Order
ACL rules in the access list should be in order of most specific to least specific
The last rule should be permit All other access
ACL Placement Rule
Standard ACL – place as close as possible to destination network or device, to avoid unnecessarily blocking traffic