## Slide 1: TNE20002 / TNE70003
Topic 6 DHCP V1.0

## Slide 2: Dynamic Host Configuration Protocol (DHCP)
All devices
PCs, switches, IPhones, printers, servers etc
need an IP address
to connect to a network

## Slide 3: Dynamic Host Configuration Protocol (DHCP)
Static IP addresses
  Devices such as routers, servers, printers, photocopiers etc, need an address that will not change
  Static address assignment is required

## Slide 4: Dynamic Host Configuration Protocol (DHCP)
Dynamic IP addresses
  PCs, Laptops in an organization often change locations, physically and logically:
    Dynamic address assignment is required
    Can use any IP address within the range of addresses in the subnet.

## Slide 5: Dynamic Host Configuration Protocol (DHCP)
DHCP
Address Allocation
MAD !

## Slide 6: DHCP Address Allocation - MAD
Automatic
Manual
Dynamic

## Slide 7: DHCP - Address Allocation Techniques - MAD
Manual
  The IP address for the client is pre-allocated
  by the administrator
  and
  DHCP conveys the IP address
  to the client.

## Slide 8: DHCP - Address Allocation Techniques - MAD
Automatic
  DHCP selects from an address pool,
  automatically assigns
  a permanent IP address to a client
  with no lease period.

## Slide 9: DHCP - Address Allocation Techniques - MAD
Dynamic
DHCP selects from an address pool
and leases the IP address to the client
for a limited period of time.

## Slide 10: Dynamic Host Configuration Protocol (DHCP)
DHCP Operation
DORA
Discover, Offer,
Request, Acknowledge
Client Action

## Slide 11: DHCP Operation – Four Messages - DORA
11
Notes: 11

## Slide 12: DHCP Operation – Four Messages - DORA
12
DHCPDISCOVER – I would like to request an address
Broadcast
DHCPOFFER – I am server 2, Here is an address, I can offer
Unicast
DHCPREQUST – I accept the IP address offer
Broadcast
DHCPACK – Your acceptance is acknowledged
Unicast
Notes: 12

## Slide 13: DHCP Operation – Obtaining a Lease – Discover
1. DHCP Discover (to Server)
  Client (PC) broadcasts DHCPDISCOVER message
  DHCPDISCOVER finds DHCP server(s)
  Uses layer 2 (FF:FF:FF:FF:FF:FF) and layer 3 broadcast addresses to communicate with server(s)

## Slide 14: DHCP Operation – Obtaining a Lease – Offer
2. DHCP Offer (to Client)
  DHCP Server
    finds available IP address to lease
    creates and ARP entry in its ARP table consisting of the MAC address of requesting host and the leased IP address
    Sends DHCPOFFER message to Client
  Unicast using server’s layer 2 MAC address as source and client’s layer 2 MAC address as destination

## Slide 15: DHCP Operation - Messages Discover and Offer
15
1. DHCP Discover
2. DHCP Offer
Offer Details
Gateway:
Notes: 15

## Slide 16: DHCP Operation – Messages Discover and Offer
16
Server Port
Client Port IP address/mask
1. DHCPDISCOVER - Broadcast
DHCP on port 67
DHCP
DHCP on port 68
? 0.0.0.0
2. DHCPOFFER - Unicast
DHCP
Notes: 16

## Slide 17: DHCP – Obtaining a Lease – Request
3. DHCP Request (to Server)
Client broadcasts DHCPREQUEST message, two purposes:
  Requests IP lease information be verified to ensure assignment is still valid
  Serves as a binding acceptance notice to the selected server and an implicit decline to any other DHCP servers that may have given the client an offer

## Slide 18: DHCP – Obtaining a Lease – Acknowledge
4. DHCP ACK (to Client)
  Server replies with unicast DHCPACK

## Slide 19: DHCP Operation – DORA Messages 1, 2, 3 and 4
19
1
2
3
4
Notes: 19

## Slide 20: DHCP – Client Action
  Client checks IP address is not a Duplicate within Subnet
  Client sends ARP request (does any host within the subnet have this IP address ?) using new IP address
  If no other hosts in subnet reply, the IP address is not a duplicate, hence it can use the IP address

## Slide 21: Configuring DHCP
21
The network statement enables DHCP on any router interfaces belonging to that network.
  The router will act as a DHCP server on that interface.
  It is also the pool of addresses that the DHCP server will use.
  Pool NaMe (vs nAmE) is case sensitive
Notes: 21

## Slide 22: Configuring DHCP
22
The ip dhcp excluded-address command configures the router to exclude an
individual address or
range of addresses when assigning addresses to clients.
IP configuration values such as the default gateway can be set.
172.16.12.1 172.16.12.10
172.16.12.254
Notes: 22

## Slide 23: Configuring DHCP – Manual Allocation
Manually allocating an IP address to a printer, photocopier etc
Router(config)# ip dhcp pool subnet12
Router(dhcp-config)# host 172.16.12.5 255.255.255.0
Router(dhcp-config)# client-identifier <unique-identifier>
The unique-identifier of the client - the printer, is specified in dotted hexadecimal notation, for example, 01b7.0813.8811.66, where 01 represents the Ethernet media type, followed by client’s MAC address
When this printer’s DHCP Client requests an IP address it will receive 172.16.12.5

## Slide 24: Configuring a Cisco Router as a DHCP Server
The Enabling the DHCP service:
  To enable the service:
  Router(config)#service dhcp
  To disable the service:
  Router(config)#no service dhcp

## Slide 25: Configuring DHCP - Options
25
Notes: 25

## Slide 26: Verifying and Troubleshooting DHCP
26
Notes: 26

## Slide 27: Verifying and Troubleshooting DHCP
show ip dhcp server statistics
show ip dhcp pool

## Slide 28: DHCP Relay
The
DHCP Server
is in a
different
subnet

## Slide 29: DHCP Relay – DHCP Server in a different subnet

## Slide 30: DHCP Relay – DHCP Server in a different subnet
IP address of Server

## Slide 31
DHCP Explained | Step by Step - YouTube
THE END