## Slide 1: TNE20002 / TNE70003
Topic 7 NAT V1.0

## Slide 2: NAT
2
Network
Address
Translation
Notes: 2

## Slide 3: Network Address Translation
3
NAT (defined by RFC 1631) is designed to conserve IP addresses and enable networks to use private IP addresses on internal networks.
These private IP addresses are translated to routable public IP addresses for accessing the Internet.
NAT translations can occur dynamically or statically.
NAT (PAT) port address translation allows multiple private ip addresses to map to the same public ip address.
Notes: 3

## Slide 4: Private addressing – Internal Networks
4
Notes: 4

## Slide 5: NAT Example
Inside Local IP address – The IP private address assigned to a host on the inside network.
Inside Global IP address – A public IP address that represents one or more inside local IP addresses to the outside world.
Outside Global IP address – The public IP address assigned to a destination host on the outside network.
Private
Public
NAT
Destination

## Slide 6: NAT Example – Private source to Public source
The translation from Private source IP address to Public source IP address.
1
2
1
2

## Slide 7: NAT Example - Public destination to Private destination
Translation back, from Public destination IP address to Private destination IP address.
3
4
3
4
.79

## Slide 8: NAT - PAT
8
Port
Address
Translation
Notes: 8

## Slide 9: NAT - PAT
Maps multiple private IP addresses to a single public IP address
Your ISP assigns one public IP address to your home router
Via PAT several of your friends can simultaneously share the this one public IP address, to surf the internet

## Slide 10: NAT - PAT
When a client opens a TCP/IP session, NAT maps a PORT number to client’s source IP address.
When a response comes back from a external server, the source port number becomes the destination port number on the return trip.
This port number determines to which client application, the packet is forwarded.

## Slide 11: PAT – Port Address Translation
Allows you to use a single Public IP address and assign it to many inside hosts
Multiple private IP addresses can be translated by a single public address (many-to-one translation).
Tracks and translates SA, DA, SP and DP (which uniquely identifies each connection) for each stream of traffic.
10.0.0.3:1555
NAT

## Slide 12: PAT Example – Two PCs using 179.9.8.80
NAT/PAT table maintains translation of:
DA, SA, DP, SP
1
2
1331
1555
Web Browsing
Web Server
NAT
PC3
PC2

## Slide 13: PAT Example Two PCs using 179.9.8.80
4
3
NAT/PAT table maintains translation of:
SA (DA), DA (SA), DP (SP)
1331
1555
PC2
PC3
PC3
PC2

## Slide 14: NAT - SAT
14
Static
Address
Translation
Notes: 14

## Slide 15: Static NAT
Uses a one-to-one mapping of private and public addresses
Mappings remain constant
Useful for web servers or hosts that must have a constant address that is accessible from the internet

## Slide 16: Configuring Static NAT
S0/0/0 Outside
Inside Fa0/0
Fa0/0
S0/0/0

## Slide 17: Dynamic NAT
Uses a pool of public addresses and assigns them on a first-come, first-served basis
When a host with a Private IP address requests access to the Internet, an ip address from the pool is allocated
The NAT Pool, the range of ip addresses available
The ACL, that permits access to the NAT pool
The Binding Statement, binding the ACL to the NAT Pool

## Slide 18: Configuring Dynamic NAT
Translate to this range of outside addresses
Source subnet IP address must match here
Binding to ACL
Inside Fa0/0
S0/0/0 Outside
Fa0/0
S0/0/0
0.0.255.255

## Slide 19: Configuring PAT – Overload on Pool
In this example a pool of Public IP addresses is used, using PAT, source ports, to differentiate between connection streams.
Inside Fa0/0
S0/0/0 Outside
10.1.0.0 0.0.255.255
ip nat pool nat-pool1 170.9.8.80 179.9.8.95
netmask 255.255.255.0
ip nat inside source list 1 pool nat-pool1 overload

## Slide 20: Configuring PAT – Overload on Interface
This is a different example, using the the outside interface S0 instead of specifying a pool of IP addresses

## Slide 21: NAT Clear Commands

## Slide 22: Verifying NAT

## Slide 23: Troubleshooting NAT/PAT
Watch the NAT translations

## Slide 24
NAT Explained | Overload, Dynamic & Static - YouTube
THE END