## Slide 1: In Lab Scenario 2 Semester 1 2022 V1.1
Student ID: 103172423
Student Name: S M Ragib Rezwan
Session Time: 2:30 to 5:30
Tutor’s Name:

## Slide 2
Kodad
(Internal)
Router
R1
Kodad
Switch S3
3650
Corporate Network Address
148.VZ.0.0/16
In Lab Scenario 2 – RIP, ACLs V1.1
G0/0/1
S0/1/1
S0/1/0
RIPv2
Routing Protocol
Bidar
(Gateway)
Router
R3
G1/0/11
ISP
Router
R4
Inter-VLAN
Routing
ISP Link
Network Address
204.3.5W.0/30
PC1
VLANXXX
PC2
VLANYYY
G1/0/13
Fa 0/24
Loopback 0
Server LAN
Database Server
Network Topology
S0/2/0
S0/1/0
A Network Configuration and Trouble Shooting Scenario
Internal
External
WRS1
Wireless
Router
Mobile
Wireless
PC
G1/0/1
VLAN1
Internet Port
VLAN1
IP address
Wireless
Connection
138.80.0.0/16
Packet Tracer
External
Server-PT
Server0
Ethernet Interface
Or
Loopback 0
If in Lab Router
44.0.0.0/8
Packet Tracer
External
Server-PT
Server1
Ethernet Interface
Or
Loopback 1
If in Lab Router
Loopback 2
159.23.0.0/16
External Network
Loopback 3
216. 12.5.0/24
External Network
Pargi
(Internal)
Router
R2
S0/1/0
S0/1/0
S0/1/1
S0/1/1
Pargi
Switch S2
2960
G0/0/1
G0/1
Inter-VLAN
Routing
“The Internet”
PC Ethernet VM
If in lab
PC VAN VM
If in lab

## Slide 3: The Scenario – An Analytical and Systematic Approach
The aim of this approach is to allow you to integrate the different topics (theory and practical) covered in the Unit, into the building of the network platform.
Each scenario requires you to build a working network, then add new network services and functionality to the network platform.
It is designed to be self re-enforcing, as what you have learnt in previous scenarios is required in future scenarios.
It emphasizes an Analytical and Systematic approach to building the network platform:
  Produce a Network Topology
  Prepare the VLSM Design
  Follow a step-by-step process to ensure that, configuration, testing, and troubleshooting is done in an order and sequence that will achieve a working network.
Doing the scenarios will prepare you for the Skills Tests
  Your tutor will provide advice and feedback only during your on campus Lab Session

## Slide 4
Scenario 2 - Introduction
This scenario can be completed independent of the lecture material as configuration details are provided on pages 15 to 27
Your tutor will give you an overview of the scenario at the beginning of the lab
You can use Packet Tracer or book a Lab Kit
As a How to Configure Guide, it is recommended you obtain a copy of “CCNA Portable Commands Guide (CCNA Self-Study) 2/3/4/5 Ed”, Scott Empson, Cisco Press
What is new?
  Creating and testing a backup path to the gateway router
  You will configure ACLs (Access Control Lists) to control the flow of traffic from each of the VLANs.
  ACLs are introduced early in the semester to give you time to appreciate their usefulness in managing the flow of IP traffic and the testing that is required to ensure they perform correctly
  You will be creating and using NAMED extended ACLs, eg:
ip access-list extended ACLVLAN70
This means the ACL is self-documenting, the above is the ACL for VLAN 70
Network Topology
  Internal, your internal network
  External, the link to the ISP and the Internet
  Use following Network addresses for Scenario 2, refer page 5 to determine V, Z and W
    Your Corporate Network Address is 148.VZ.0.0/16
    Your ISP Link Address is 204.3.5W.0/30

## Slide 5
How to determine your Network Addresses and VLAN Numbers
Rule Set A
Network Addresses – (Example Only, use your Student ID)
  eg student Id
    Nine digit Id 123057210 (from Left to Right)
    If Seven digit Id 3057210 then 993057210 (from Left to Right)
  Rule 1: If the Corporate Network Address is 148.VZ.0.0/16 where V is seventh number and Z is last number in your student ID
    V=2 and Z=0, hence 148.20.0.0/16 is your Corporate Network Address
  Rule 2: If the ISP Link Address is 204.3.5W.0/30 where W is eighth number in your student ID
    W=1, hence 204.3.51.0 is your ISP Link Address
VLAN Numbers – (Example Only, use your Student ID)
  eg student Id
    Nine digit Id 123057210
    If Seven digit Id 3057210 then 993057210
  Rule 1: VLAN XXX where XXX are the last three numbers in you student ID
  Rule 2: VLAN YYY where YYY are the middle three numbers in you student ID
  Rule 3: IF XXX = YYY then XXX = XXX + 1
  Rule 4: VLAN 130, IF XXX or YYY =130 then 130 - 3 = 127
  Appling Rules
    Rule 1: VLAN XXX: XXX= 210 hence VLAN210
    Rule 2: VLAN YYY: YYY=057 hence VLAN57
    Rule 3: No need to apply
    Rule 4: No need to apply

## Slide 6
Scenario 2 Addresses and VLAN Numbers
Record your Network Addresses and VLAN Numbers
Refer Rule Set A
Your Student ID: 103172423
Your Corporate Network Address 148.VZ.0.0/16 V= 4 Z= 3
Your ISP Link Address 204.3.5W.0/30 W= 2
Your VLAN Numbers : XXX= 423 yyy= 172

## Slide 7: Task 2 VLSM Design – Use VLSM Calculator Paste Below

## Slide 8: Scenario 2 -Tasks
1. Do not configure enable passwords OR line console passwords on router and switches, unless specified by the task
2. Internal Network VLSM Design - Paste in page 7
a) Design IP VLSM Addressing Scheme with following requirements::
  Refer rules page 5
  Switch S1 VLAN XXX Eggs 1200 hosts
  Switch S1 VLAN 1 18 hosts
  Switch S2 VLAN YYY Milk 100 host
  Switch S2 VLAN 130 Bread 50 hosts (130 may change, refer rules page 7)
  Switch S2 VLAN 1 18 hosts
  3 Internal Serials 2 hosts each
  Bidar Database Server LAN loopback 0 18 hosts
b) Document assignment of ip addresses to router interfaces and PC Hosts
c) Use a VLSM calculator
3. Cable Connection – Refer Network Topology Diagram
a) Connect Kodad router to switch S3 G1/0/11
b) Connect Pargi router to switch S2 G0/1
c) Check routers are connected via serial links
d) Connect PC1 to switch S3 G1/0/13 using the patch panel, connect PC2 to switch S2 Fa 0/24 using the VAN
e) If using Packet Tracer connect Servers to ISP via ethernet cables
4. Helpful Configurations
a) Configure the line console on each router and switch, as shown below:
line console 0
logging synchronous (stops system messages overwriting your typing)
exec-timeout 0 0 (ensures you do not return to user executive mode)
b) Turn off DNS (Domain Name Service)
no ip domain-lookup (ensures if you miss-type a command, the router will not try to resolve the command as a URL web address)
5. Message of the Day (MOTD) Banner Configuration
You must configure a MOTD Banner, recording your student id, family name and lab time, on all routers and switches, as shown below:
banner motd &
Welcome to Hostname
Your Student Id, Your Family Name, Your Session Time
&
6. Device Host Names
a) All devices must be configured with a host name eg KodadR1, KodadS1 etc

## Slide 9: Scenario 2 -Tasks
7. Switch Configuration
a) Refer to pages 20 to 23 and to your journal and lab exercises from prior unit on Basic Switch and VLAN Configuration
b) Check the switch is clean, if NOT then:
i) Delete the vlan.dat file to remove old VLANs from the Switch, use - delete vlan.dat
ii) Use - erase startup-config then reload
c) On switch S3 3650
  create VLAN XXX Eggs
  configure ports G1/0/13, G1/0/14 as VLAN XXX access ports
  configure Port Security, mac address sticky on ports G1/0/13, G1/0/14 max 4, with violation shutdown
d) On switch S2 2960
  create VLAN YYY Milk, VLAN 130 Bread (130 may change, refer rules page 7)
  configure port 24 as VLAN YYY as access port
  If in Lab Kit - configure a static mac address, VLAN YYY, on Fa 0/24 to the MAC address of PC2
  If Packet Tracer - configure Port Security, mac address sticky on Fa 0/24 max 1, with violation protect
e) On S2 configure G0/1 as a trunk port, On S3 configure G1/0/11 as a trunk port
f) Switch Management – on both switches configure an ip address on interface VLAN 1 and configure a default gateway
g) Configure enable password cisco and Line vty with password cisco and login, so each switch can be accessed via Telnet
8. Trouble Shooting VLANs
a) To check VLANs created, use – show vlan brief
9. Trouble Shooting Port Security
a) To check port security is enabled, use - show port-security
b) A table will be displayed showing the security status of the switch ports
10. Network IP Address Configuration
a) Configure ALL router serial and loopback interfaces with ip addresses and descriptions
b) Configure Packet Tracer Servers with ip addresses, connect to ISP via ethernet cable
c) Kodad and Pargi Routers
i) Refer page 19 and to your journal and lab exercises from prior unit on Basic Inter-VLAN Routing
ii) Configure Inter-VLAN routing on G0/0/1
  - Kodad configure separate sub-interfaces for VLAN 1 (the management VLAN) and VLAN XXX
  - Pargi configure separate sub-interfaces for VLAN 1 (the management VLAN) and VLAN YYY
  - Configure each sub-interface with an ip address and description
d) Configure PC1 and PC2 Hosts with specified VLAN:
i) IP address and subnet mask.
; ii) Default Gateway IP address.
e) Check default gateway configured on both switches

## Slide 10: Scenario 2 -Tasks
11. Trouble Shooting Trunking – between each Switch and its Router
a) To check Trunking is activated, on switch(es), use – show interface trunk
b) Check correct interface has been configured for trunking !
12. Trouble Shooting Point-to-Point Single Link Testing
a) This test is to check that each individual link in the network is working.
b) Ping
– ensure you can ping from one end of each serial link to the other:
  PC to Router in same subnet/VLAN/network.
  PC to PC in same subnet/VLAN/network.
  Router to each direct neighbour Router over a serial link.
c) Link NOT working ? - Common problems:
  Physical connection not made.
  The clock rate is not configured on DCE interface of a serial link.
  An incorrect IP address or subnet mask is configured on one interface of a link
  The interface is shutdown.
13. Trouble Shooting Inter-VLAN Routing Test
a) This test is to check Inter-VLAN routing is working
b) PC1 ping VLAN 1 ip address of Switch S1, PC1 telnet to Switch S1
c) PC2 ping VLAN 1 ip address of Switch S2, PC2 telnet to Switch S2
d) Check IP address/Mac address mapping on the router, show arp
14. Routing Protocol Configuration (refer pages 17,18)
a) Kodad and Pargi
  RIP V2
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
b) Bidar
  RIP V2, do not advertise the external network address
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
  Configure default route to ISP Router
  Advertise default route to internal routers
c) ISP Router
  Do not configure RIP
  Only configure a static route (default class B mask) to your internal network
  Configure loopbacks for Web Servers (If you are using Packet Tracer may need to use Server Devices)

## Slide 11: Scenario 2 -Tasks
15. Trouble Shooting Routing - Presence of Subnets
a) Internal Routers
- Use show ip route to display the routing table on each router:
- Check all the subnets are present
- Check there is a default route
b) External Router
- Use show ip route to display the routing table:
- Check there is static route back to your internal network
c) Common problems:
  Routing protocol is not advertising a subnet
  An interface is down
  Internal serial links, IP addresses/masks incorrect
  Static or Default route not configured
16. Trouble Shooting End-to-End Path Testing
a) This test is to check that the routing - static and dynamic, is working.
b) Ping from PC1 Host in VLAN XXX to External Web Servers (the Internet)
c) Ping from PC2 Host in VLAN YYY to External Web Servers (the Internet)
d) Ping from PC1 Host in VLAN XXX to PC2 Host in VLAN YYY
e) Use traceroute to pin point problems.
f) Use debug ip icmp on ISP router to check ping request arrives
g) Check if a subnet is missing from a routing table, use - show ip route
h) End-to-End Path Test Failed ? - Common problems:
  Default gateway IP address not configured on a PC.
  PC connected to incorrect interface.
  Incorrect static route on ISP
  Subnet not advertised
  Default route not propagated/Gateway of last resort not set
17. Trouble Shooting Switch Management
a) Check that you have remote access to each switch, from PC1 telnet to each switch

## Slide 12: Scenario 2 -Tasks
18. Trouble Shooting Testing Backup Link
a) On router Pargi determine current exit interface to destination Database Server Lan – show ip route
b) Shut down the interface
c) Did backup route, install in the routing table ? – show ip route
19. Wireless Router Configuration
a) You will configure a Wireless Router and connect it to the fixed network infrastructure.
b) Refer to page 27 and Wireless Supporting Material
c) On WRS1 Wireless Router configure:
i) Internet Port with VLAN 1 IP address ii) SSID as W<student id> iii) DHCP to provide addresses for Wireless LAN PCs and your Mobile Phone
iv) allow inbound ping requests v) Do not configure wireless security
d) Connect a straight through UTP cable between Kodad Switch S3 G1/0/1 (port in VLAN1) and Internet Port (in VLAN1) on Wireless Router
e) VLAN 1 will carrier wireless traffic
f) On ISP Router use – debug ip icmp
g) Configure a wireless end device to ping the Internet
h) From Wireless End Device, Ping the Internet
20. HTTP Servers
a) On In Lab Routers
  Configure a HTTP server on ISP Router, use – ip http server
b) Packet tracer
  If you are using Packet Tracer you must configure Web Servers and connect the servers to the ISP Router
c) Allows you to test your ACLs using a Browser.

## Slide 13: Scenario 2 - Tasks
21. Access List Requirements Kodad Router
a) Refer Lab Exercises on Access Control Lists
b) You must create a NAMED Extended ACL for VLAN XXX based on following requirements:
  PCs in VLAN XXX denied HTTP access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router and permit ALL other access to this Server or Loopback and the Internet
  PCs in VLAN XXX permitted only HTTP access to ISP Packet Tracer Server1 or ISP Loopback 1 if in Lab Router and deny ALL other access to this Server or Loopback
  PCs in VLAN XXX denied all access to ISP Loopback 2
  PCs in VLAN XXX permitted ALL access to the rest of The Internet.
  ALL means IP
c) You need to be analytical and systematic in our approach to translating the above requirements into a set of rules – the ACL statements, which
then must be tested to ensure the above requirements have been satisfied:
i) Create a NAMED Extended ACL for VLAN XXX using the template on page 17, refer Task 22
ii) Test the ACL for VLAN XXX refer Task 23
22. Creating and Configuring NAMED Access Lists on Kodad Router
a) Refer Lab Exercises on Access Control Lists
b) Use Notepad to create your ACLs, note ACL names are case sensitive eg aclvan70 and Aclvlan70 are different acls
c) Identify each requirement then configure an ACL rule for each requirement.
d) Create a NAMED access list in Notepad, consider the ordering of the rules, use the following structure:
! Deletes previous version of access list
no ip access-list extended ACLVLAN<Id>
! Insert Latest version of access list
ip access-list extended ACLVLAN<Id>
<Your ACL rules, refer template on page 17>
! For most situations this should be the last rule ie permit all other access to “The Internet”
permit ip any any
e) Combine ACL rules as required to form your access list, carefully consider the order in which the rules should be arranged, refer pages 17,18
f) Paste ACL from Notepad into router (router must be in global configuration mode)
g) Configure ACL on correct interface

## Slide 14: Scenario 2 - Tasks
23. Trouble Shooting Access Lists on Kodad Router
It is important to verify that the ACL rules actually work as intended, refer to the steps below:
  1. Use show access-lists
    If all rules tested go to 5
    Else Identify which rule you want to test
  2. Use clear access-list counters
    Clear any counts against the rules
  3. Go to PC in VLAN<Id> perform test eg Ping, Telnet, Browser etc to trigger a match with the identified rule
  4. Use show access-lists
  Was the identified rule matched ?
    Yes – rule action correct, Repeat process, go to 1
    No – Debug
      Was another rule matched ?
      Where no rules matched ?
      Check syntax and order of rules – make changes – Repeat process go to 1
5. Trouble Shooting completed

## Slide 15: Scenario 2 – ACL Templates
ACL for VLAN XXX on Kodad Router
The Access List – Extended Named (create the ACL in Notepad, then paste into router config mode)
no ip access-list extended ACLVLANXXX (Delete previous version of the ACL for VLAN XXX )
Ip access-list extended ACLVLANXXX (Self-documenting, the ACL for VLAN XXX, ! means comment)
! Rule 1 - Deny ONLY HTTP access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router
deny tcp source subnet wildcard (inverse of subnet mask) destination host ip address eq www
! Rule 2.1 - Permit ONLY HTTP access to ISP Packet Tracer Server1 or ISP Loopback 1 if in Lab Router
permit tcp source subnet wildcard (the inverse of subnet mask) destination host ip address eq www
! Rule 2.2 - Deny all other access to ISP Packet Tracer Server1 or ISP Loopback 1 if in Lab Router
deny ip source subnet wildcard (inverse of subnet mask) destination host ip address
! Rule 3 - Deny IP access to ISP Loopback 2
deny ip source subnet wildcard (inverse of subnet mask) destination host ip address
! Rule 4 - Permit ALL other access
permit ip any any
ACL Placement - On Sub Interface G0/0/1.XXX on Kodad Router
interface G0/0/1.XXX
ip access-group ACLVLANXXX in (This access list is filtering inbound ip traffic from VLAN XXX to the router)

## Slide 16: Scenario 2 – ACL Overview
ACL Case Sensitivity
ACL names are case sensitive eg aclvlan70 and AclVlan70 are different ACLs
Should decide to use either all uppercase - ACLVLAN70 or all lowercase – aclvlan70 names to reduce errors
ACL Rule Order
ACL rules in the access list should be in order of most specific to least specific
The last rule should be permit All other access
ACL Placement Rules
Standard ACL – place as close as possible to destination network or device, to avoid unnecessarily blocking traffic to other destinations
Extended ACL – place as close as possible to source network or device, to block traffic early to reduce network congestion
ACL Trouble Shooting Commands
show access-lists (shows all access lists)
clear access-list counters (clears ip packet hits against a rule)
Refer Task 23

## Slide 17: Routing Configuration Rules
Each router should only advertise its internal directly connected networks
Routing updates must not be sent to LANs/VLANs
A default route to the Internet should only be configured on the gateway router
Only the gateway router must advertise the default route to the internal routers
The ISP router should have a static route pointing to the corporate’s Network with the relevant class A, B, C default mask
Do not configure the ISP router with a routing protocol advertising the corporate’s network

## Slide 18: RIP Configuration
Configure on Kodad Router
router rip
version 2 (Version 2 supports VLSM)
network 148.VZ.0.0 (Advertise the internal network)
passive-interface G0/0/1.1 (Do not send routing updates to LAN subnets)
passive-interface G0/0/1.XXX (Do not send routing updates to LAN subnets)
Configure on Bidar Router
ip route 0.0.0.0 0.0.0.0 S0/2/0 (The default route to the Internet)
router rip
version 2
network 148.VZ.0.0
default-information originate (Advertise default route to other internal routers)
passive-interface loopback 0 (Do not send routing updates to Database Server LAN)
Configure on Pargi Router
What do you think ?
Configure on ISP Router (RIP is not configured in ISP)
ip route 148.VZ.0.0 255.255.0.0 S0/1/0 (ISP configure a static route to internal network)

## Slide 19: Inter-VLAN Routing Configuration
Configure on the required Router
interface G0/0/1
description The Physical Interface
no shutdown
interface G0/0/1.1
description A logical Sub Interface
description VLAN 1 VLAN Management
encapsulation dot1q 1
ip address <dotted decimal> <subnet mask>
interface G0/0/1.<vlan id>
description A logical Sub Interface
description VLAN <vlan Id> <vlan name>
encapsulation dot1q <vlan id>
ip address <dotted decimal> <subnet mask>
etc ……

## Slide 20: Switch Configuration
Switch S3 - Configure VLANs
vlan XXX
name Eggs
Switch S2 - Configure VLANs
vlan YYY
name Milk
vlan 130 (130 may change, refer rules page 5)
name Bread
Switch S3 and S2
  Configure IP address for management vlan
interface vlan 1
ip address <ip address> <mask>
  Configure Default Gateway
ip default-gateway <ip address of router interface> (Use VLAN 1 subinterface IP address)

## Slide 21: Switch Configuration
Configure a switch ACCESS port (note you can specify a range of switch ports):
interface fa 0/3 (or interface range fa 0/3 – 5)
switchport access vlan <number> (assigns port to a vlan)
switchport mode access (sets port to access, for PCs)
switchport port-security (enables port security, do not forget this command)
switchport port-security maximum 1 (maximum of 1 mac address(es) can stick)
switchport port-security mac-address sticky
switchport port-security violation shutdown (shuts down port, default when security turned on)
OR
switchport port-security violation protect (protects, but does not shut down the port)
Configure a static MAC address entry in Mac Address Table
mac address-table static AAAA.BBBB.CCC vlan YYY interface fa 0/24
(replace AAAA.BBBB.CCCC with the mac address of the PC)

## Slide 22: Switch Configuration
Configure a switch TRUNK port on a Switch
2960 Series Switch
interface G0/1
switchport mode trunk (sets port to trunk)
3650 Series Switch
interface G1/0/11
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation
switchport mode trunk (sets port to trunk)
3560 Series Switch
interface Fa0/1
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation)
switchport mode trunk (sets port to trunk)

## Slide 23: Switch Commands
Managing the MAC Address Table
show mac address-table (displays entries in table)
show mac address-table dynamic (displays only dynamic entries in table)
clear mac address-table (deletes all entries from table)
clear mac address-table dynamic (deletes only dynamic entries from table)
Re-activating a switch port that has been violated
When a violation causes a switch port to block traffic, it must be re-activated
This is achieved by doing a shutdown then a no shutdown on the switch port, refer below:
interface fa0/10
shutdown
(wait until shutdown confirmed)
no shutdown

## Slide 24: How to configure SSH – Secure Shell
1. Configure switch or router with a hostname:
hostname S1
2. Configure a local user account:
username labuser privilege 15 secret cisco (always use cisco as password)
3. Configure domain name:
ip domain-name scenario.lab
4. Configure SSH Certificate:
crypto key generate rsa general-keys modulus 1024
5. Configure Line vty
line vty 0 15 (4 for a router)
transport input SSH
login local
end

## Slide 25: PC Command Window Useful Trouble Shooting Commands
ipconfig
  Allows you check your PC’s addresses
  ipconfig /all
  ipconfig /? for help
netstat
  Displays the TCP/IP network protocol statistics and information
  netstat –a
  netstat –e
  netstat –s
  netstat /? for help
nbtstat
  Displays protocol statistics and current TCP/IP connections
  nbtstat –n
  nbtstat /? for help

## Slide 26: PC Command Window Useful Trouble Shooting Commands
arp
  Displays the Address Resolution table
  arp -a
  arp /? for help
route print
  Displays the routing table of your PC
  route /? for help
ping
  ping 127.0.0.1 Checks your PC’s IPv4 Protocol stack
  ping 192.168.1.10 ping a destination
  ping /? for help
tracert
  Traces individual hops to the destination
  tracert 192.168.1.10
  tracert /? for help

## Slide 27: In Lab - Configuring the Wireless Router – Linksys WRT300N Also refer Wireless Supporting Material A and B
Power UP wireless router (get a wireless router from your tutor)
Reset it to factory default – push reset button and hold until blue symbols flash
Start up PC Ethernet VM, configure to obtain ip address automatically
Ethernet Connection – plug blue UTP cable from your PC into any Ethernet port (1 to 4) on the wireless router
Open DOS Command Window – type ipconfig /all to confirm PC Ethernet has been obtained an ip address from wireless router
Use a Browser to connect to factory default ip address 192.168.1.1 on the wireless router
Authentication – username: admin, password: admin
Wireless Router Setup
  Ensure you always click save at the bottom of each screen
  Internet Setup
    Internet Connection type: static IP
    Assign an ip address from VLAN 1 address range
  Network Setup - DHCP
    For Wireless PCs
    Use address space for wireless LAN
  Disable/Enable PC Ethernet LAN connection to pick up a new ip address from Wireless LAN address space
  Use a Browser to re-connect to new (default gateway) ip address on the wireless router
  Security
    Disable Firewall
  Wireless Wi-Fi Protected Setup
    Wireless Configuration: manual
    SSID: student Id
Use a Wireless End Device to connect to the Wireless Router refer below:
  Look for the wireless tray icon – bottom right, click
  Associate with the wireless LAN broadcasting your student ID as its SSID
  Open DOS Command Window – type ipconfig /all to confirm an ip address has been obtained from wireless router
  From your Laptop PC Ping default gateway on the wireless router to confirm connection is working
  Wireless Router - Remove blue UTP cable from your PC, get a new blue UTP cable, plug into Internet Port
  Connect new blue UTP cable to Desk Top coloured enclosure port, then patch from patch panel to switch S3 G1/0/1 from your Laptop PC Ping to default gateway for VLAN 1 to confirm the connection is working