## Slide 1: In Lab Scenario 6 Semester 1 2022 V1.1
Student ID:
Student Name:
Session Time:
Tutor’s Name:

## Slide 2
Nagri
(Internal)
Router
R1
Nagri
Switch S3
3650
Your part of the Private Network Address Space
VZ.40.0.0/13
In Lab Scenario 6 - PPP, CHAP V1.1
G0/0/1
S0/1/0
S0/1/0
Use ONLY
OSPF Routing Protocol
Daspur
(Gateway)
Router
R2
G1/0/11
ISP
Router
R3
Trunk for Inter-VLAN
Routing
ISP PPP WAN Link
Network Address
210.11.W.0/30
PC1
VLANXXX
PC2
VLANYYY
G1/0/13
G1/0/24
Loopback 0
Server LAN
Database Server
Network Topology
S0/1/1
S0/1/1
PC VAN VM
If in lab
PC Ethernet VM
If in lab
A Network Configuration and Trouble Shooting Scenario
Internal
External
NAT Public
Address POOLS
Connection to rest of
Internal network
“The Internet”
154.3.0.0/16
Packet Tracer
External
Server-PT
Server0
Ethernet Interface
OR
Loopback 0
if in Lab Router
18.0.0.0/8
Packet Tracer
External
Server-PT
Server1
Ethernet Interface
OR
Loopback 1
if in Lab Router
Loopback 2
162.55.0.0/16
External Network
Loopback 3
201.12.80.0/24
External Network

## Slide 3: The Scenario – An Analytical and Systematic Approach
The aim of this approach is to allow you to integrate the different topics (theory and practical) covered in the Unit, into the building of the network platform.
Each scenario requires you to build a working network, then add new network services and functionality to the network platform.
It is designed to be self re-enforcing, as what you have learnt in previous scenarios is required in future scenarios.
It emphasizes an Analytical and Systematic approach to building the network platform:
  Produce a Network Topology
  Prepare the VLSM Design
  Follow a step-by-step process to ensure that, configuration, testing, and troubleshooting is done in an order and sequence that will achieve a working network.
Doing the scenarios will prepare you for the Skills Tests
  Your tutor will provide advice and feedback only during your on campus Lab Session

## Slide 4
Scenario 6 - Introduction
This scenario can be completed independent of the lecture material as configuration details are provided on pages 21 to 34
Your instructor will give you an overview of the scenario at the beginning of the lab
As a How to Configure Guide, it is recommended you obtain a copy of “CCNA Portable Commands Guide (CCNA Self-Study) 2/3/4/5 Ed”, Scott Empson, Cisco Press
What is new?
  You will configure a PPP WAN Link
  You will configure CHAP Authentication on a PPP WAN Link
  NAT Overload
  ACLs to deny a VLAN access to Database Server LAN
  DHCP and the use of a helper ip address
  Book a kit in the lab to do this scenario, to prepare you for Skills Test B
Network Topology
  Internal, your internal network
  External, the link to the ISP and the Internet
  Use following Network addresses for Scenario 6, refer page 7 to determine V, Z and W
    The Corporate Private Network Address, VZ.0.0.0/8.
    The corporate address has been divided up and you have been given the address space VZ.40.0.0/13 to build your part of the Corporate Network.
    ISP Link Address, 210.11.W.0/30
    NAT Public Address Pool, provided by the ISP is 135.12.64.0/25, refer page 23

## Slide 5
How to determine your Network Addresses and VLAN Numbers
Rule Set C
Network Addresses – (Example Only, for Scenario 6 use network addresses on page 6 and use your student ID)
  eg student Id
    Nine digit Id 123057210 (Left to Right)
    If Seven digit Id 3057210 then 993057210 (Left to Right)
  Rule 1: If the Corporate Network Address is VZ.0.0.0/8 where V is sixth and Z is fifth number in your student ID
    V=7 and Z=5, hence 75.0.0.0/8 is your Corporate Network Address
  Rule 2: If the ISP Link Address is 191.22.4W.0/30 where W is eighth number in your student ID
    W=1, hence 191.22.42.0 is your ISP Link Address
VLAN Numbers – (Example Only, use your Student ID
  eg student Id
    Nine digit Id 123057210 (Left to Right)
    If Seven digit Id 3057210 then 993057210 (Left to Right)
  Rule 1: VLAN XXX where XXX are the fifth, sixth and seventh numbers in you student ID
  Rule 2: VLAN YYY where YYY are the sixth, seventh and eighth numbers in you student ID
  Rule 3: IF XXX = YYY then XXX = XXX + 1
  Rule 4: VLAN 516 , IF XXX or YYY = 516 then 516 - 3 = 519
  Appling Rules
    Rule 1: VLAN XXX : XXX= 572 hence VLAN572
    Rule 2: VLAN YYY: YYY=721 hence VLAN721
    Rule 3: No need to apply
    Rule 4: No need to apply

## Slide 6
Scenario 6 Addresses and VLAN Numbers
Record your Network Addresses and VLAN Numbers
Refer Rule Set C
Your Student ID:
Your section of Corporate Network Address space VZ.40.0.0/12 V= Z =
    Your ISP Link Address 210.11.W.0/30 W =
Your VLAN Numbers

## Slide 7: Task 2 VLSM Design – Use VLSM Calculator Paste Below

## Slide 8: Scenario 6 -Tasks
1. VLSM Design
a) Rules refer page 5
b) As a first task it is important to get your addressing scheme correct and documented. Design IP VLSM Addressing Scheme, using this part VZ.40.0.0/12 of Corporate Network Address space with:
  VLAN XXX Dogs 800 hosts
  VLAN YYY Cats 200 hosts
  VLAN 516 Birds 120 hosts (516 may change, refer rules page 5)
  Daspur Database Server LAN loopback 0 20 hosts,
  VLAN 1 6 hosts,
  Internal Serial 2 hosts
c) You can use a VLSM calculator
d) Paste in page 7

## Slide 9: Scenario 6 -Tasks
2. Do not configure enable passwords OR line console passwords on router and switches, unless specified by the task
3. Cable Connection
a) Connect Nagri router to switch port G0/1
b) Check routers are connected via serial links, refer to page 2
c) Connect PC1 to G1/0/13 S3, connect PC2 to G1/0/24 S3
4. Helpful Configurations
a) Configure the line console on each router and switch, as shown below:
line console 0
logging synchronous (stops system messages overwriting your typing)
exec-timeout 0 0 (ensures you do not return to user executive mode)
b) Turn off DNS (Domain Name Service)
no ip domain-lookup (ensures if you miss-type a command, the router will not try to resolve the command as a URL web address)
5. Message of the Day (MOTD) Banner Configuration
You must configure a MOTD Banner, recording your student id, family name and session time, on all routers and switches, as shown below:
banner motd &
Welcome to Hostname
Your Student Id, Your Family Name, Your Session Time
&
6. Device Host Names
a) All devices must be configured with a host name eg NagriR1, NagriS1 etc

## Slide 10: Scenario 6 -Tasks
7. Switch Configuration
a) Refer to pages 28 to 31 and to your journal and lab exercises from prior unit on Basic Switch and VLAN Configuration
b) Check the switch is clean, if NOT then:
i) Delete the vlan.dat file to remove old VLANs from the Switch, use - delete vlan.dat
ii) Use - erase startup-config then reload
  c) Create VLAN XXX Dogs, VLAN YYY Cats, VLAN 516 Birds (516 may change, refer rules page 5)
d) Configure G0/1 as a trunk port
e) Configure as access ports, only VLAN XXX ports G1/0/13, G1/0/14 and VLAN YYY port G1/0/24
f) Switch Management – configure an ip address on interface VLAN 1 and configure a default gateway
g) Configure enable password cisco and Line vty with password cisco and login, so each switch can be configured via Telnet
h) Configure Port Security, VLAN XXX , mac address sticky on ports G1/0/13, G1/0/14 max 2, with violation protect
i) if Lab Kit - Configure a static mac address on G1/0/24 use the MAC address of PC2
j) If Packet Tracer - configure Port Security, mac address sticky on G1/0/24 max 1, with violation protect
8. Trouble Shooting VLANs
a) To check VLANs created, use – show vlan brief
9. Trouble Shooting Port Security
a) To check port security is enabled, use - show port-security
b) A table will be displayed showing the security status of the switch ports

## Slide 11: Scenario 6 -Tasks
10. Network IP Address Configuration
a) Configure ALL the router serial and loopback interfaces with ip addresses, refer Task 1 and Task 2
b) Nagri Router
i) Inter-VLAN Routing Configuration
  Refer page 27 and to your journal and lab exercises from prior unit on Basic Inter-VLAN Routing
  Configure Inter-VLAN Routing on G0/0/1
  Only create separate sub-interfaces for VLANs 1, XXX and YYY
  Assign each sub-interface with an ip address
c) PC Configuration
i) Configure PC1 and PC2 IP addresses
d) Nagri Switch
    Check default gateway configured on switch, use VLAN1 G0/0/1 .1 sub-interface ip address
11. Trouble Shooting Trunking – between Switch and Router
a) To check Trunking is activated, on switch(es), use – show interface trunk
b) Check correct interface has been configured for trunking !

## Slide 12: Scenario 6 -Tasks
12. Trouble Shooting Point-to-Point Single Link Testing
a) This test is to check that each individual link in the network is working.
b) Ping (command) – ensure you can ping from one end of each link to the other:
  PC to Router in same subnet/VLAN/network.
  PC to PC in same subnet/VLAN/network
  Switch to Router
  Router to each direct neighbour Router over a serial link.
c) Link NOT working ? - Common problems:
  Physical connection not made.
  An incorrect IP address or subnet mask is configured on one interface of a link
  The interface is shutdown.
13. Trouble Shooting Inter-VLAN Routing Testing
a) This test is to check Inter-VLAN routing is working
b) Ping PC1 – VLAN XXX to PC2 – VLAN YYY
c) Ping PC1 – Switch 1
d) On Nagri Router – show arp, to check the IP address to MAC address mapping
14. Trouble Shooting Telnet to Switch
a) To check you can telnet to the switch
b) From PC1 DOS command window – telnet to the switch
c) Common problems:
  Switch Vlan1 interface shutdown
  Switch has no default gateway IP address
  Switch Line vty not configured with login and password
  Inter-VLAN routing failure

## Slide 13: Scenario 6 -Tasks
15. Routing Protocol Configuration (refer pages 24 to 26)
a) Nagri
  OSPF using wildcards for each subnet
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
b) Daspur
  OSPF using wildcards for each subnet
  Do not advertise the external network address
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
  Configure default route to ISP Router
  Advertise default route to Nagri Router
c) ISP Router
  Do not configure OSPF
  Configure loopbacks for Web Servers (If you are using Packet Tracer may need to use Server Devices)
16. Trouble Shooting OSPF Neighbor Adjacency
a) Verify that the routers have formed an adjacency with each other, use - show ip ospf neighbor
b) Adjacency NOT Formed ? - If an adjacency has not formed it could be due to:
i) subnet masks on each end of link do not match
ii) the directly connected subnet is not included in the network statements
c) Other trouble shooting commands: show ip protocols, debug ip ospf events
17. Trouble Shooting Routing - Presence of Subnets
a) Internal Routers
- Use show ip route to display the routing table on each router:
- Check all the subnets are present
- Check there is a default route
b) Common problems:
  Routing protocol is not advertising a subnet
  An interface is down
  Static or Default route not configured

## Slide 14: Scenario 6 -Tasks
18. Trouble Shooting Internal Private End-to-End Path Testing
a) This test is to check that the internal routing - static and dynamic, is working.
b) Use debug ip icmp on Daspur router to check ping request arrives
c) Ping from PC Hosts in VLAN XXX and VLAN YYY to Database Server on Daspur
d) Use traceroute to pin point problems.
e) Internal Private End-to-End Path Test Failed ? - Common problems:
  Default gateway IP address not configured on a PC.
  PC connected to incorrect interface.
  Subnet not advertised
  Subnet missing from routing table
  Default route not advertise
19. NAT Configuration
    a) Configure NAT Pools on the Daspur Router
    - Refer to page 23 and Lab on NAT Configuration
    - Create separate NAT Pools and ACLs for VLANs 1, XXX, YYY
    - Overload each NAT pool
    b) ISP router
- Configure a static route to the public NAT Pool address on Daspur
20. Trouble Shooting NAT - Internal Private to External Public End-to-End Path Testing
a) This test is to check that NAT is working - that the private IP address is being translated to a public IP address
b) Use debug ip nat on Daspur to view the NAT translations
c) Use debug ip icmp on ISP router to check ping request arrives
d) Ping from PC Hosts in VLAN XXX and VLAN YYY to the Internet – pick an External Web Server
e) NAT Failed ? – Common Problems:
  ACL and Pool names are case sensitive, check names are correct
  ACL incorrectly configured
  NAT pool incorrectly configured
  Binding of ACL to NAT Pool incorrectly configured
  Inside and outside interfaces incorrectly or not configured
  On ISP static route is not pointing to NAT pool
f) Useful commands, use - show ip nat translations, debug ip nat

## Slide 15: Scenario 6 -Tasks
21. DHCP Configuration – Dynamic IP address allocation
    Configure DHCP on Daspur Router
    Configure helper ip address for DHCP on Nagri Router
    Refer to page 23 and Lab on DHCP Configuration
    Create separate DHCP Pools for VLANs XXX and YYY
    Exclude the first four IP addresses
    Configure PC1 and PC2 to obtain IP address automatically
22. Trouble Shooting DHCP
a) Use debug ip dhcp server events on Daspur Router, to view the DHCP process
b) Open DOS CMD window on PC1 and PC2 – ipconfig /release then ipconfig /renew
c) Addresses obtained ? NO – check router configuration,
use – show ip dhcp pool, show ip dhcp binding, show run
23. HTTP Servers
a) On In Lab Routers
  Configure a HTTP server on ISP Router, use – ip http server
b) Packet tracer
  If you are using Packet Tracer you must configure Web Servers and connect the servers to the ISP Router
c) Allows you to test your ACLs using a Browser
24. Telnet Access to Routers
a) Configure line vty with password cisco and login, so you can connect to each router can via Telnet
b) NO enable password is required as you are NOT configuring the router
c) This allows you to test your ACLs using Telnet.

## Slide 16: Scenario 6 - Tasks
25. Point-to-Point Protocol (PPP) Configuration
a) Configure the link between Daspur and ISP routers as PPP link, refer to page 32
b) Ping across the link between Daspur and ISP to check it is working
26. CHAP Configuration
a) Configure, refer to page 33, CHAP authentication on the link between Daspur and ISP
27. Trouble Shooting CHAP
a) Ping across the link between Daspur and ISP
b) Ping failed ? – Common problems:
  Host name incorrectly configured
  Password incorrectly configured with space at front
  Encapsulation incorrectly configured
c) To check authentication, use - debug ppp authentication

## Slide 17: Scenario 6 - Tasks
28. Access List Requirements
a) Refer to pages 19 to 21 and Lab Exercises on Access Control Lists
b) You must create a NAMED Extended ACL for VLAN XXX based on following requirements:
  PCs in VLAN XXX permitted HTTP access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router and denied ALL other access to this Server.
  PCs in VLAN XXX denied PING request to PCs in VLAN YYY
  PCs in VLAN XXX permitted PING reply to PCs in VLAN YYY
  PCs in VLAN XXX permitted ALL access to the Internet – all the external Servers
c) You must create a NAMED Extended ACL for VLAN YYY based on following requirements:
  PCs in VLAN YYY denied ALL access to Database Server LAN
  PCs in VLAN YYY permitted ALL access to the Internet – all the external Servers
  ALL means IP
d) You must create NAMED Standard ACLs to control Telnet access to the routers based on following requirements:
  ONLY PCs in VLAN XXX permitted TELNET access to Nagri Router
  ONLY PCs in VLAN XXX denied TELNET access to Daspur Router
e) You need to be analytical and systematic in our approach to translating the above requirements into a set of rules – the ACL statements, which
then must be tested to ensure the above requirements have been satisfied:
i) Create a NAMED Extended ACL for VLAN XXX using the template on page 19, refer Task 29
ii) Test the ACL for VLAN XXX refer Task 30
iii) Create a NAMED Standard ACLs for Telnet access using the template on page 20 refer Task 29
iv) Test the ACLs for Telnet access refer Task 30

## Slide 18: Scenario 6 - Tasks
29. Creating and Configuring NAMED Access Lists
a) Refer Lab Exercises on Access Control Lists
b) Use Notepad to create your ACLs, note ACL names are case sensitive eg aclvanXXX and AclvlanXXX are different acls
c) Identify each requirement then configure an ACL rule for each requirement.
d) Create a NAMED access list in Notepad, consider the ordering of the rules, use the following template:
! ACL for VLAN <No> on Router <router name>
! Deletes previous version of access list
no ip access-list extended ACLVLAN<No>
! Insert Latest version of access list
ip access-list extended ACLVLAN<No>
<Your ACL rules follow>
! For most situations this should be the last rule ie permit all other access to “The Internet”
permit ip any any
e) Combine ACL rules as required to form your access list, carefully consider the order in which the rules should be arranged.
f) Paste ACL from Notepad into router (router must be in global configuration mode)
g) Configure ACL on correct interface
30. Trouble Shooting Access Lists
It is important to verify that the ACL rules actually work as intended, refer to the steps below:
  1. Use show access-lists
    If all rules tested go to 5
    Else Identify which rule you want to test
  2. Use clear access-list counters
    Clear any counts against the rules
  3. Go to PC in VLAN<Id> perform test eg Ping, Telnet, Browser etc to trigger a match with the identified rule
  4. Use show access-lists
  Was the identified rule matched ?
    Yes – rule action correct, Repeat process, go to 1
    No – Debug
      Was another rule matched ?
      Where no rules matched ?
      Check syntax and order of rules – make changes – Repeat process go to 1
5. Trouble Shooting completed

## Slide 19: Scenario 6 - ACL Templates
ACL for VLAN XXX on Nagri Router
The Access List – Extended Named (create in Notepad, then paste into router config mode)
no ip access-list extended ACLVLANXXX (Delete previous version of the ACL for VLAN XXX )
ip access-list extended ACLVLANXXX (Self-documenting, the ACL for VLAN XXX, ! means comment)
! Only permit HTTP access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router
permit tcp source subnet wildcard host ip address eq www
! Deny ALL other access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router
deny ip source subnet wildcard host ip address
! Permit ping reply (echo-reply) to a destination – PCs in VLAN YYY subnet
permit icmp source subnet wildcard destination subnet wildcard echo-reply
! Deny PING request to a destination - PCs in VLAN YYY subnet
deny icmp source subnet wildcard destination subnet wildcard
! Permit access to The Internet
permit ip any any
ACL Placement - On Sub Interface G0/0/1.XXX on Nagri Router
interface G0/0/1.XXX
ip access-group ACLVLANXXX in

## Slide 20: ACL Templates
ACL to control Telnet Access to Nagri and Daspur Routers
The Access List – Standard Named (create in Notepad, then paste into router config mode)
! On Nagri
no ip access-list standard ACLTELNET
ip access-list standard ACLTELNET
! Permit VLANXXX Telnet Access to Nagri
permit source subnet wildcard
deny any
! On Daspur
no ip access-list standard ACLTELNET
ip access-list standard ACLTELNET
! Deny VLANXXX Telnet Access to Daspur
deny source subnet wildcard
permit any
Interface Placement - line vty 0 4, on Nagri and Daspur Routers
line vty 0 4
password cisco
login
access-class ACLTELNET in

## Slide 21: Scenario 6 - ACL Overview
ACL Case Sensitivity
ACL names are case sensitive eg aclvlanXXX and AclVlanXXX are different ACLs
Should decide to use either all uppercase - ACLVLANXXX or all lowercase – aclvlanXXX names to reduce errors
ACL Rule Order
ACL rules in the access list should be in order of most specific to least specific
The last rule should be permit All other access
ACL Placement Rules
Standard ACL – place as close as possible to destination network or device, to avoid unnecessarily blocking traffic
Extended ACL – place as close as possible to source network or device, to block traffic earlier to reduce congestion
ACL Trouble Shooting
show access-lists
clear access-list counters
Use the following for testing the rules: ping, telnet, a browser

## Slide 22: DHCP Configuration
Configure DHCP pools on Router Daspur
service dhcp (turns on DHCP service)
ip dhcp pool poolVLANXXX
network subnetwork subnetwork mask
default-router ip address of G0/0/1.XXX
ip dhcp pool poolVLANYYY
network subnetwork subnetwork mask
default-router ip address of G0/0/1.YYY
Configure on Router Nagri
  Configure an ip helper address, refer Lab on DHCP Configuration
Trouble Shooting Commands
  show ip dhcp pool
  show ip dhcp binding
  clear ip dhcp binding *
  debug ip dhcp server events
  open DOS CMD window on PC1 and PC2 – ipconfig /release then ipconfig /renew

## Slide 23: NAT Configuration
Configure on Router Daspur
  The NAT Public Address Pool, provided by the ISP is 135.12.64.0/25, this is a range of ip addresses, divide 3 ways, do not VLSM
  Address Pool Nat Pools
ip nat pool POOLVLANXXX starting IP address ending of IP address> netmask ?.?.?.?
ip nat pool POOLVLANYYY starting IP address ending of IP address> netmask ?.?.?.?
  ip nat pool POOLVLAN1 starting IP address ending of IP address> netmask ?.?.?.?
  NAT Access Control Lists
  ip access-list extended ACLVLANXXX
  permit ip source subnet wildcard any
  ip access-list extended ACLVLANYYY
  permit ip source subnet wildcard any
  ip access-list extended ACLVLAN1
  permit ip source subnet wildcard any
  Establish dynamic source translation by binding the pools with the access control lists
  ip nat inside source list ACLVLANXXX pool POOLVLANXXX
  ip nat inside source list ACLVLANYYY pool POOLVLANYYY
  ip nat inside source list ACLVLAN1 pool POOLVLAN1
  Specify inside and outside interfaces:
  interface s0/1/0
  interface s0/1/1
  interface loopback 0
  Overload each NAT pool – refer Lab on NAT Configuration
Trouble Shooting Commands
  show ip nat translations
  clear ip nat translation *
  show ip nat statistics
  debug ip nat
  debug ip nat detailed

## Slide 24: Routing Configuration Rules
Each router should only advertise its internal directly connected networks
Routing updates must not be sent to LANs/VLANs
A default route to the Internet should only be configured on the gateway router
Only the gateway router must advertise the default route to the internal routers
The ISP router
  If the company is using:
    a public network address, the ISP should have a static route pointing to the corporate’s public Network with the relevant class A, B, C mask
    a private network address, the ISP should have a static route pointing to the corporate’s public NAT Pool with relevant mask
Do not configure the ISP router with a routing protocol advertising the corporate’s network

## Slide 25: OSPF Configuration ONLY if Specified
Configure on Internal Nagri Router
router OSPF 9 (9 is just a process id, routers may use different process ids)
network ?.?.?.? ?.?.?.? area 0 (VLAN XXX, ospf routers exchange updates with routers in the same area)
network ?.?.?.? ?.?.?.? area 0 (VLAN YYY, ? wildcard is inverse of subnet mask)
network ?.?.?.? ?.?.?.? area 0 (VLAN 1 wildcard is inverse of subnet mask)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Nagri to Daspur)
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on Internal Gateway Daspur Router
router OSPF 10
network ?.?.?.? ?.?.?.? area 0 (Loopback Database LAN)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Nagri to Daspur)
ip route ?.?.?.? ?.?.?.? S0/1/1 (The default route to the Internet)
default-information originate (Advertise default route to other internal routers)
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on External ISP Router (OSPF is not configured in ISP)
ip route ?.?.?.? ?.?.?.? S0/1/1 (ISP configure a static route to Public NAT Pool)

## Slide 26: EIGRP Configuration ONLY if Specified
Configure on Internal Router
router EIGRP 15 (15 is the autonomous system number, both routers need to use the same number in order to exchange updates)
network ?.?.?.?> ?.?.?.? (wildcard is inverse of subnet mask, ? means insert)
“
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on Gateway Router
router EIGRP 15
network ?.?.?.? ?.?.?.? (wildcard is inverse of subnet mask, ? means insert)
“
ip route 0.0.0.0 0.0.0.0 S0/1/1 (The default route to the Internet)
redistribute static (Advertise default route to other internal routers)
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on ISP Router (EIGRP is not configured in ISP)
ip route ?.?.?.? ?.?.?.? S0/1/1 (ISP configure a static route to Public NAT Pool)

## Slide 27: Inter-VLAN Routing Configuration
Configure on the required Router
interface G0/0/1
description The Physical Interface
no shutdown
interface G0/0/1.1
description A logical Sub Interface
description VLAN 1 VLAN Management
encapsulation dot1q 1
ip address address subnet mask
interface G0/0/1.vlan id
description A logical Sub Interface
description VLAN vlan Id vlan name
encapsulation dot1q vlan id
ip address address subnet mask
etc ……

## Slide 28: Switch Configuration
Configure VLANs
vlan XXX
name Dogs
vlan YYY
name Cats
vlan 615
name Birds (615 may change, refer rules page 7)
Configure IP address for management vlan
interface VLAN 1
ip address address mask (This allows the switch to be configured remotely via Telnet)
Configure Default Gateway
ip default-gateway ip address of router interface (Use VLAN 1 subinterface IP address)

## Slide 29: Switch Configuration
Configure a switch ACCESS port (note you can specify a range of switch ports):
interface fa 0/3 (or interface range fa 0/3 – 5)
switchport access vlan <number> (assigns port to a vlan)
switchport mode access (sets port to access, for PCs)
switchport port-security (enables port security, do not forget this command)
switchport port-security maximum 1 (maximum of 1 mac address(es) can stick)
switchport port-security mac-address sticky
switchport port-security violation shutdown (shuts down port, default when security turned on)
OR
switchport port-security violation protect (protects, but does not shut down the port)
Configure a static MAC address entry in Mac Address Table
mac address-table static AAAA.BBBB.CCC vlan YYY interface fa 0/24
(replace AAAA.BBBB.CCCC with the mac address of the PC)

## Slide 30: Switch Configuration
Configure a switch TRUNK port
2960 Series Switch
interface G0/1
switchport mode trunk (sets port to trunk)
3650 Series Switch
interface G0/1
switchport mode trunk (sets port to trunk)
3560 Series Switch
interface Fa0/1
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation)
switchport mode trunk (sets port to trunk)

## Slide 31: Switch Commands
Managing the MAC Address Table
show mac address-table (displays entries in table)
show mac address-table dynamic (displays only dynamic entries in table)
clear mac address-table (deletes all entries from table)
clear mac address-table dynamic (deletes only dynamic entries from table)
Re-activating a switch port that has been violated
When a violation causes a switch port to block traffic, it must be re-activated
This is achieved by doing a shutdown then a no shutdown on the switch port, refer below:
interface fa0/10
shutdown
(wait until shutdown confirmed)
no shutdown

## Slide 32: PPP Configuration
Configure on Router Daspur
interface S0/1/1
description Link to ISP
ip address address subnet mask
encapsulation ppp
no shutdown
Configure on Router ISP
interface S0/1/1
description Link to Daspur
ip address address subnet mask
encapsulation ppp
no shutdown
PPP Trouble Shooting Commands
  debug ppp negotiation
  debug ppp packet

## Slide 33: CHAP Configuration – Create User Accounts
Configure on Router Daspur
username ISP password cisco (username and password are case sensitive)
interface S0/1/1
ppp authentication chap
Configure on Router ISP
username Daspur password cisco
interface S0/1/1
ppp authentication chap
The Password Problem
  You need to ensure the password does not have spaces at the front or the end else the authentication will fail
PPP Trouble Shooting Commands
  debug ppp authentication

## Slide 34: How to configure SSH – Secure Shell
1. Configure switch or router with a hostname:
hostname S1
2. Configure a local user account:
username labuser privilege 15 secret cisco (always use cisco as password)
3. Configure domain name:
ip domain-name scenario.lab
4. Configure SSH Certificate:
crypto key generate rsa general-keys modulus 1024
5. Configure Line vty
line vty 0 15 (4 for a router)
transport input SSH
login local
end

## Slide 35: PC Command Window Useful Trouble Shooting Commands
ipconfig
  Allows you check your PC’s addresses
  ipconfig /all
  ipconfig /? for help
  To request the DHCP server to release or renew the PC’s IP address use:
    ipconfig /release, ipconfig /renew
netstat
  Displays the TCP/IP network protocol statistics and information
  netstat –a
  netstat –e
  netstat –s
  netstat /? for help
nbtstat
  Displays protocol statistics and current TCP/IP connections
  nbtstat –n
  nbtstat /? for help

## Slide 36: PC Command Window Useful Trouble Shooting Commands
arp
  Displays the Address Resolution table
  arp -a
  arp /? for help
route print
  Displays the routing table of your PC
  route /? for help
ping
  ping 127.0.0.1 Checks your PC’s IPv4 Protocol stack
  ping 192.168.1.10 ping a destination
  ping /? for help
tracert
  Traces individual hops to the destination
  tracert 192.168.1.10
  tracert /? for help